EUROPEAN UNION									OPERATIONAL PROGRAMME ON

European Regional									‘TRANSPORT’ 2007-2013

Development Fund									The nearer, the closer …

Cohesion Fund

Update of the scenario,

based on the transport model

developed under ЕММЕ software,

as part of the ‘General Transport Master Plan’

FINAL REPORT

April 2013

institute of transport and communications

Contents

Introduction	8

1.	Purpose and scope of the project	9

2.	Brief description of the transport model of GTMP, subject to update and inferences	11

2.1	Structure of the model	11

2.1.1	BMPT	11

2.1.2	BMCT	13

2.2	Baseline year	13

2.3	Forecasts for future periods	13

2.3.1	Forecast on the demand for passenger transport under ‘Do minimum’ scenario	14

2.3.2	Forecast on the demand for freight transport under ‘Do minimum’ scenario	16

2.4	Procedure of updating the transport model elaborated by the Contractor for GTMP	18

2.5	Conclusions concerning possibilities for model update and identification of ‘bottlenecks’ on the road and railway network	19

3.	Selection of a baseline year, system of zoning and scope of the infrastructure networks	21

4.	Update of the model of passenger services against a new baseline year	27

4.1	Travel by passenger car	28

4.2	Travel by coach transport	35

4.3	Travel by railway transport	39

4.4	Conclusions about demand for passenger services in 2011.	45

4.5	Freight services by automobile transport	47

4.5.1	Domestic freight services	47

4.5.2	Import and export by automobile transport	48

4.5.3	Transit automobile transport	48

4.5.4	Interzone freight services by automobile transport	48

4.6	Freight services by railway transport	51

4.7	Conclusions about demand for freight services in 2011.	53

4.8	Passenger and freight traffic on the road network	55

5.	Update of forecasts on factors influencing the demand for passenger services	57

5.1	Forecast on the growth in GDP	57

5.2	Demographic forecast	59

5.3	Degree of motorization	61

5.4	Price of time	62

5.5	Transport costs	63

5.6	Summary of the input data for projection models	63

6.	Forecast on the demand for passenger services	64

7.	Forecast on the demand for freight transport	65

7.1	Forecast on the domestic freight services	65

7.2	Forecast on the international freight services	66

8.	Modeling the infrastructure networks by 2020.	67

9.	Assignment of projected passenger and freight traffic to the models of infrastructure networks	68

9.1	Passenger services	68

9.2	Freight services	73

9.3	Identification of bottlenecks	78

Schedules	84

List of figures

Fig. 1 	Diagram of the Bulgarian transport model	11

Fig. 2 	View of the title screen of the interface for update	18

Fig. 3 	System of zoning, domestic zones	22

Fig. 4 	System of zoning, partially international zones 	23

Fig. 5 	Modeled road network in Bulgaria for the baseline year 2011.	25

Fig. 6	Scope of the modeled railway network in Bulgaria for the baseline year 2011.	26

Fig. 7	Comparison between modeled and registered intensity of passenger car for the baseline year 2011.	31

Fig. 8	The 50 destinations with busiest traffic for daily interzone trips by passenger car	32

Fig. 9	The 50 destinations with busiest traffic for business interzone trips by passenger car	33

Fig. 10	The 50 destinations with busiest traffic for private interzone trips by passenger car	34

Fig. 11	The 50 destinations with busiest traffic for interzone trips by coach	37

Fig. 12	Average 24-hour number of passengers in 2011 by sections of the road network (by passenger car and coach)	38

Fig. 13	Stations with more than 100 000 passengers for 2011.	40

Fig. 14	The 25 busiest destinations for interzone trips on accelerated fast trains	41

Fig. 15	The 25 busiest destinations for interzone trips on fast trains	42

Fig. 16	The 50 busiest destinations for interzone trips in passenger trains	43

Fig. 17	Passengers carried by railway transport in 2011 on sections of the railway network	44

Fig. 18	Distribution of passenger trips in 2011 by mode of transport (public and individual)	46

Fig. 19	Freight carried by automobile transport in 2011 by sections of the road network	50

Fig. 20	Freight carried by railway transport in 2011 by sections of the railway network	52

Fig. 21	Distribution of demand for freight transport services in 2011 by mode of transport (automobile and railway)	54

Fig. 22	Comparison between modeled and registered intensity of traffic of MTV for the baseline year 2011.	55

Fig. 23	Average 24-hour yearly intensity of interzone automobile traffic on the NRN for 2011.	56

Fig. 24	Comparison between the GDP growth projected in GTMP and the updated one	58

Fig. 25	Backlog in the updated GDP growth by districts / regions against the forecast from GTMP	59

Fig. 26	Summarized forecast on the growth in passenger services by mode of transport	65

Fig. 27	Summarized updated forecast on the growth in freight overalnd services	68

Fig. 28	Projected yearly number of passengers by automobile transport (PC and coach) for 2020.	69

Fig. 29	Projected yearly number of passengers by automobile transport (PC and coach) for 2030.	70

Fig. 30	Projected yearly number of passengers by railway transport for 2020.	71

Fig. 31	Projected yearly number of passengers by railway transport for 2030.	72

Fig. 32	Projected freight traffic in tons by automobile transport for 2020.	74

Fig. 33	Projected freight traffic in tons by automobile transport for 2030.	75

Fig. 34	Projected freight traffic in tons by railway transport for 2020.	76

Fig. 35	Projected freight traffic in tons by railway transport for 2030.	77

Fig. 36	Average 24-hour yearly intensity of automobile traffic by 2020	79

Fig. 37	Average 24-hour yearly intensity of automobile traffic by 2030	80

Fig. 38	Comparison between average 24-hour yearly intensity of automobile traffic by 2020 and throughput of the road network by sections	81

Fig. 39	Comparison between average 24-hour yearly intensity of automobile traffic by 2030 and throughput of the road network by sections	82

List of tables

Table 1	Description of forecasts on the social-economic and demographic factors used in BTM	16

Table 2	Comparison between the projected population growth for 2011 from BMPT and the actual one reported from the National 2011 census.	19

Table 3	Population by regions and planning areas by към 01.02.2011	27

Table 4	Calibrated parameters for obtaining matrixes of the synthetic automobile trips	28

Table 5	Values of the price of time for passenger trips for 2008 and 2011.	29

Table 6	An example of NSI data for the daily labour trips	30

Table 7	Estimated average 24-hour number of interzone trips by passenger car for the baseline year 2011	31

Table 8	Estimated average 24-hour number of interzone trips by coach for the baseline year 2011	36

Table 9	Estimated average 24-hour number of trips by railway	39

Table 10	Distribution of demand for passenger services by mode of transport and market segments for the baseline 2011	45

Table 11	Freight carried by automobile transport in 2011 under domestic services by commodity groups	47

Table 12	Freight services by automobile transport in 2011 by market segments	49

Table 13	Freight services by railway transport in 2011 by market segments	51

Table 14	Freight carried by railway transport in 2011 by commodity groups	51

Table 15	Distribution of demand for interzone freight transport services by commodity groups and mode of transport for the baseline year 2011.	53

Table 16	Growth in GDP in accordance with the medium-term forecast for 2014 - 2016 of the Government	57

Table 17	Summarization of the updated forecast for growth in GDP on the national level	58

Table 18	Forecast on the population by regions and planning areas	60

Table 19	Forecast on the active population by regions and planning areas	61

Table 20	Updated forecast on the degree of motorization	62

Table 21	Updated forecast on the price of time by purpose of the trip	62

Table 22	Summarization of input data for the forecast models	63

Table 23	Variations of growth in the generated passenger trips by zones	64

Table 24	Share of passenger services by form of transport	65

Table 25	Summarized forecast on the growth in passenger services	65

Table 26	Forecast on the growth in domestic freight services by automobile and railway transport from BMFT	66

Table 27	Updated summarized forecsat on the growth in domestic freight services by automobile and railway transport	66

Table 28	Summarized updated forecast on growth in the freight overland services	68

List of abbreviations

| MW | Motorway |
| --- | --- |
| RIA | Road Infrastructure Agency |
| CBA | Cost-Benefit Analysis |
| GDP | Gross Domestic Product |
| BDZ | Bulgarian State Railways |
| BMPT | Bulgarian Model of Passenger Transport |
| BMFT | Bulgarian Model of Freight Transport |
| BTM | Bulgarian Transport Model |
| ‘CAA’ DG | ‘Civil Aviation Administration’ Directorate General |
| GD | General Directorate |
| BCP | Border Checkpoint |
| ‘NRIC’ SE | ‘National Railway Infrastructure Company’ State Enterprise |
| EEC | European Economic Community |
| EC | European Commission |
| EU | European Union |
| RTA | Road Traffic Act |
| EA | Executive Agency |
| PC | Passenger Car |
| MTV | Motor Transport Vehicle |
| MTITC | Ministry of Transport, Information Technology and Communications |
| MF | Ministry of Finance |
| NCNT | National Commodity Nomenclature for Transport |
| NSI | National Statistical Institute |
| GTMP | General Transport Master Plan |
| OP | Operational Programme |
| pkm | Passenger-kilometer, transport of one passenger over a distance of 1 kilometer |
| NRN | National Road Network |
| SRR | Sofia Ring Road |
| tkm | Ton-kilometer, transport of one ton over a distance of 1 kilometer |
| €ct | eurocent |
| GPS | Geographic Positioning System |
| HS | Harmonized System |
| TEN-T | Trans European Network – Transport |

# Introduction

The present report was prepared by the Institute of Transport and Communications Ltd. in its capacity as Contractor in the Update of the scenario based on the transport model developed under ЕММЕ software, as part of the ‘General Transport Master Plan’ project.

This report presents the process of updating the transport model of the General Transport Master Plan (GTMP) in conformity with the approach proposed and presented by the Contractor in the Introductory Report from January 2013.

The updated transport model was delivered to the Contracting Authority on 16.04.2013, while this report presents the main results and inferences about:

- Updated base year of the model – 2011, and

- forecasts for the years 2020 and 2030.

# Purpose and scope of the project

In accordance with the Technical Specification it is required from the Contractor to ‘perform an update of the scenario based on the transport model developed under EMME software, as part of the General Transport Master Plan’. The Contractor ought to identify with the thus updated model the ‘bottlenecks’ in the transport network of this country in view of prioritizing investments in the core and the comprehensive network in the roads and railway sector with a 2020 and 2030 horizon. It shall be possible to use results from the updated scenario in the determination of investments in the two main sectors with relevant strategies/ plans/ programmes being developed/updated on their basis.’

In order to achieve the objectives indicated here above the Contractor ought:

- To update the transport model developed in 2008/2009 by ’incorporating therein the changes occurred in the forecasts for the development of this country’s economy and its major trading partners, as well as in the transport network of the country and the levels of traffic’. The minimum scope of the information that ought to be updated includes:

- economy: the forecast for changes in the GDP, the commodity circulation and fuel prices;

- demography: data from the latest census in 2011 and a forecast on its change;

- transport: data on the traffic and forecasts for the development of passenger and freight transport on the national road and railway networks.

The Contracting Authority does not require from the project Contractor to have in its possession the software for developing transport models with which the model of GTMP (ЕММЕ/3) was derived. It is specified that the model can be updated also under a similar software package, such as PTV VISUM, for which the Contractor holds a full license.

- To identify the ‘bottlenecks’ in the national road and railway networks (core and comprehensive) based on the ‘revised forecasts by 2020 and 2030 on the basis of the current economic forecasts and the incorporation of completed projects and projects in the process of implementation’.

The ultimate results of all work on the project ought to be a comparison between transport flows and the existing capacity of the transport network presented in the form of a map showing the sections of transport networks in which demand is close to the available capacity or exceeds it.

The Contracting Authority delivered on 17.01.2013 to the Contractor the entire information available on the GTMP in electronic form. Following a detailed review and analysis the Contractor came proposed the following approach for the update:

Step 1:	Update of the model of passenger trips to a new baseline year

Step 2:	Preparation of a new model of the overland freight transport by the baseline year

Step 3:	Forecast on the demand for passenger trips

Step 4:	Demand on the demand for freight transport

Step 5:	Modeling the infrastructure networks by 2020

Step 6:	Assignment of forecast passenger and freight traffic on the respective infrastructure networks and identification of the bottlenecks

The Approach was approved and accepted by the Contracting Authority. A huge quantity of data and information was collected and processed for the update of the baseline year, a considerable quantity of which – from executive agencies, government enterprises and firms to the Ministry of Transport, Information Technology and Communications.

# Brief description of the transport model of GTMP, subject of update and inferences

## Structure of the model

The structure of the Bulgarian transport model, as described by the Author of GTMP, is displayed in the diagram below.

Bulgarian transport model (BTM)

Bulgarian Model of Passenger Transport		Bulgarian Model of Freight Transport

(BMPT)						(BMFT)

Passenger     Coach		Railway		Cargo		Railway 	  Waterway 	Air

car			transport		truck		transport    transport	transport

EMME/3 Model (E3)		E3 & ET			Electronic tables (ET)

Fig. 1 	Diagram of the Bulgarian transport model

Basically, the model consists of two major parts – a model of the passenger transport (BMPT) and a  model of the freight transport (BMFT). BMPT comprises 3 forms of transport – automobile, coach and railway. BMFT comprises 4 forms of transport – automobile, railway, waterway and air. BMPT was fully developed in the environment of the software product for transport modeling ЕММЕ/3, which means that all 4 traditional steps (generation, attraction, distribution and assignment) were modeled for execution in an EMME/3 environment. In contrast to the passenger transport the freight model was produced in the form of electronic tables and the assignment of automobile cargo transport (and not the freight railway one) was effected in ЕММЕ/3 environment only.

### BMPT

BMPT includes the following six main components, as presented in brief here below.

Supply model

The model of supply includes:

- A model of the road network comprising 19 thousand km of motorways, first, second and third-class roads and the speed function under the respective four categories depending on traffic intensity; the model represents to a large extent the level of construction of the road network by the baseline year 2008.

- Model of the coach ‘network’ representing in its essence the timetables of intercity coach lines by the baseline year 2008.

- Model of the railway ‘network’, which in similarity to the coaches, contains the supply of railway passenger services, i.e. the timetable of passenger trains by the base year.

Model of demand

The demand model for passenger services represents a set of 16 matrixes of origin and purpose of passenger trips by:

- three forms of transport, as indicated here above – automobile, railway and coach

- three purposes of travel – business, leisure and commuting

- for two categories of passengers – those possessing a passenger car and the ones that have no car.

The system of zoning adopted for the model consists of a total of 314 zones – 272 domestic zones for the country and 42 international zones – outside the territory of the country.

Specific models for assignment by mode of transport

Such models describe the routes of services where alternative ones are available. A model has been used in which generalized travel costs are minimum.

Models of behaviour

The models of behaviour model the choice made by passengers between available forms of transport in response to changes introduced in the generalized costs of travel on one or more modes of transport. These models are two-step ones: in the first place the choice is modeled between private and public transport, and if the public one is opted for – the choice is modeled between coach and railway transport.

The four sub-models specified above refer to the base year 2008. Another two models have been developed for the need of forecasting.

Model of growth

This model reflects the influence of changes in demographic and social-economic factors on the future demand for passenger transport.

Model of private automobiles ownership

The results of this model are used as input data for the behavioural model and influence on the choice of mode of transport.

### BMFT

The model of freight transport consists of three individual sub-models, respectively, for the railway, waterway and air transport, with the BMFT for the freight automobile transport being connected with BMPT in the following manner:

- They use a unified database

- Data from the road network model (supply) are used as input ones for the model of demand for heavy-load trucks services

- The projected increase in demand for heavy cargo traffic is used reversely as input data in the passenger services model in order to reflect the influence of this traffic on travel time and choice of a route for passenger services.

Freight services are modeled for 5 groups of commodities on the grounds of a zoning system consisting of 9 domestic regions, 2 ports and 12 international zones (7 states and 5 additional regions). International transport of freight (import, export and transit) are modeled separately by way of individual models based on electronic tables.

Although it is not expressly indicated it ought to be expected that the model of demand would consist of 20 matrixes, respectively for:

- 4 forms of transport – automobile, railway, waterway and air transport, and

- 5 commodity types – connected, respectively, with the agrarian sector, with industry (mining, processing and construction), with trade, with the other services and containers.

## 2.2	Baseline year

The model as a whole is calibrated, validated and approved by the base year 2008, so that it can reproduce the existing demand (of transport services) by the relevant year with the respective level of accuracy. Matrixes refer to the demand for transport on a work day in the interval from 7:00 through 19:00 hrs.

## 2.3	Forecasts for future periods

The model of GTMP works with two projected horizons – 2015 and 2030, while the intermediate years are obtained by way of interpolation. Demand is estimated for two standard alternative scenarios of transport sector development:

- ‘Minimum development’ (Do minimum) and

- ‘Project realization’ (Do something).

The ‘Do minimum’ scenario represents the base scenario for the transport situation during the projected year, which is the result of the influence of factors external for the transport sector – demographic, social-economic and/or political. In essence, this variant models the future development as a continuation of the status-quo in this sector.

In essence, the second scenario represents a set of different possible alternatives for intervention in the sector, both in the infrastructure and in the supply of transport services.

### 2.3.1	Demand on demand for passenger transport under the Do minimum scenario

The forecast for passenger transport demand was produced by growth models that use factors of growth in the demand for freight transport by the base year 2008 depending on various factors  of influence. The external factors influencing passenger transport demand and are modeled in BMPT, are as follows:

- Count of population and number of the economically active population by 9 regions (linear dependence)

- Growth in the Gross Domestic Product and degree of motorization, also by 9 regions (increase with elasticity against the respective indicator).

The distribution of projected demand by form of transport is defined as a function of changed generalized costs for the competitive modes of transport that depend on fuel prices, tariffs of services on coach and railway transport and price of time by forms of transport.

In contrast to the demand model for the baseline year developed with a high level of detail, the model of growth for projected horizons was developed for 9 zones partially corresponding to the zones of planning:

- Northwestern

- Northern Central

- Northeastern

- Stara Zagora

- Remaining part of Eastern zone

- Southern Central

- Sofia city and region

- Blagoevgrad and

- Remaining part of Southwestern zone.

The following table presents the input demographic and social-economic factors used in the BMPT.

|  | Baseline year 2008 | Projections | Notes |
| --- | --- | --- | --- |
|  |  | 2015 | 2030 |  |
| Economic factors |
| GDP | 30,782 million Euro | +23% | +139% | GDP growth is given at regional level (Table 2.2) |
| GDP per capita | 4,028 Euro/capita | 5,139 Euro/capita (+28%) | 10,952 Euro/capita (+172%) | Projected passenger demand is based on GDP per capita at regional level (Table 2.17) |
| Demographic factors |
| Total population | 7.76 million | 7.49 million (or -3.5% on 2008 figure) | 6.88 million (or -11.3% on 2008 figure) | Projected passenger demand is based on GDP per capita at regional level (Table 2.6) |
| Active population | 3.63 million | 3.51 million (or -4.0% on 2008) | 3.20 million (or -11.8% on 2008 figure) | Projected passenger demand is based on the growth in active population at regional level (Table 2.8) |
| Transport costs |
| Price of fuel | 1.28 Euro/liter | 1.13 Euro/liter | 1.23 Euro/liter | Source: Forecast of the Consultant (as shown in Table 2.13) |
| Transport vehicle efficiency | 0.0712 liter/km | 0.0653 liter/km (-8.2%) | 0.0546 liter/km (-23.3%) | Source: Forecast of the Consultant (as shown in Table 2.14) |

|  | Baseline year 2008 | Projections | Notes |
| --- | --- | --- | --- |
|  |  | 2015 | 2030 |  |
| Public transport prices | Railway 0.0331 Euro/km Coach 0.0588 Euro/km | Railway 0.0331 Euro/km Coach 0.0588 Euro/km | Railway 0.0384 Euro/km Coach 0.0947 Euro/km | Source Data of the operator. Discussion in Section 2.5.5 of this document. (See Table 2.15) |
| Ownership of means of transport |
| Ownership of means of transport | 0.276 autos/ person | 0.309 autos/ Person (+12%) | 0.412 autos/ Person (+49%) | Discussion in Section 2.6 of this document. The forecast on passenger demand is based on the growth in ownership of means of transport at regional level. (See Table 2.17) |

| Transport network |
| --- |
| Change in the transport network |  | Includes three transport projects that are in construction | Includes three transport projects that are in construction | It is envisaged that the influence of these three projects on total demand is unimportant and therefore not taken into consideration. |
| Assessment of time for travel |
| ATT – business | 19.77 Eurocent/min. | 23.42 Eurocent/min. | 39.58 Eurocent/min. | Source: Requirements to the making of CBA in the Transport Sector’ for Bulgaria |
| ATT – non-business | 7.30 Eurocent/min. | 8.65 Eurocent/min. | 14.61 Eurocent/min. | As per above. |

Table 1	Description of forecasts on the social-economic and demographic factors used in BTM

Based on the thus projected changes in the factors influencing the demand for passenger transport estimation matrixes were prepared for a 12-hour interval of a work day in number of passengers by form of transport by the respective projected horizon (2015 and 2030). Matrixes were assigned on the respective networks that were not changed by the base year 2008.

‘Bottlenecks’ in the automobile network are identified with the projected intensity of passenger cars traffic being compared with the throughput of the respective road segment determined on the basis of its class and gauge. It does not become clear from the data presented in GTMP Main Report 3 whether matrixes of coach services have been assigned in addition to the matrixes of passenger car travels, and also more importantly – the estimation matrixes of freight automobile transport.

No information is provided in the report mentioned above about results from the assignment of matrixes of railway services, although there are data on a change in the number of passengers by lines.

### 2.3.2	Demand on demand for freight transport under the Do minimum scenario

Like the passenger transport forecast, the demand on demand for freight transport was produced with models of growth against the base year 2008. An electronic table was used, which divides the growth factor by origin, function or aggregated by origin-function. Growth factors are determined separately for:

- the 5 groups of commodities (it. 1.2)

- 3 modes of transport:

- domestic automobile transport

- railway transport, and

- waterway transport through ports.

Owing to the absence of data on the import and export with automobile transport a different methodology was applied in the determination of the future growth factors based on a correlation between import and export by the surveyed commodity groups and the growth in GDP. It does not become clear from the description of this approach what the basis was for estimating the transit freight traffic.

Forecasts on the railway and river transport on the River Danube were produced in number of heavy-load automobiles and not in tons.

Identified are the following factors that have influence on the future demand for freight transport:

- Changes in the number of population and migration that were projected in connection with BMPT

- Growth in GDP, also projected in BMPT, and production growth by economic sectors

- Growth in the economy of main trading partners

- Change in the trade models mostly depending on the development of the economy of the host country, but also connected with a change in the political environment, such as for example, accession to the EU

- Change in the relativ costs by mode of transport and respectively, in the relatrive attractiveness of railway and waterway transport

- Other factors, such as operation of cargo trucks of greater load-carrying capacity, logistic centers, border procedures.

Based on individual forecasts part of the above indicators have served for the calculation of growth factors by market segments, in electronic table format: domestic automobile services, import and export through the ports, import, export and transit by automobile and railway transport (also presented generally, without commodity groups). Matrixes in GTMP Main Report 3 are generalized and do not present details concerning the mode of transport and the type of commodity.

The forecast on domestic freight services on rail was produced by utilizing a different classification, so-called ‘expanded’ classification of freight by 7 groups of commodities designated indicatively as:

- Agriculture

- Coal

- Metals

- Construction

- Petroleum

- Chemicals

- Other.

The forecast was produced as a direct dependence between the production of the respective sector of the economy and the demand for transport services.

A third, different classification of freight was used in the demand on freight services on the River Danube, comprising 8 groups of commodities:

- Automotive industry

- Chemicals

- Coal products

- Construction materials/mixes

- Food or agricultural products

- Metal products

- Products of the oil refining industry

- Other.

As a result of these calculations an aggregate forecast was produced of freight services demand with automobile and railway transport, both on domestic and international traffic (import, export and transit) as a total number of heavy-load transport vehicles (with no specification of the group of commodity) for a 12-hours interval on a work day by 2015 and 2030.

Forecasts for the traffic through ports are by commodity groups, in tons and per year, which were subsequently recalculated in heavy-load automobiles.

No information is presented in Main Report 3 about results from the assignment of freight matrixes for automobile and/or railway transport on the infrastructure networks. Absent is quantitative information about the intensity of freight traffic both on roads and along the railway networks. Indication is made of growth factors in matrix form (9х9).

## 2.4	Procedure of updating the transport model elaborated by the Contractor for GTMP

User interface was elaborated to GTMP, which facilitates the extraction of data on the traffic by a particular year and a concrete scenario with ‘Project realization;.

The interface is activated on a personal computer following standard installation of the ‘setup.exe’ installation file with a launcher window being loaded to enable the selection of a working language (Bulgarian or English) and option for review of available data or choice of a new test.

Fig. 2 	View of the title screen of the interface for update

This interface allows the update of the following variables:

- Growth in GDP based on the selected 9 geographic ‘sectors’ corresponding to the zones specified in it. 2.3.1

- Population growth for the same sectors

- Growth in the active population for the same sectors

- Fuel price for a passenger car

- Fuel consumption per mileage unit of a passenger car

- Growth in public transport prices (coach and railway) against the baseline year.

All other changes in BMPT, as well as in BMFT, to the extent they use a single data base, are determined in advance and fixed as invariables. Their change requires new modeling in an ЕММЕ/3 environment.

Comparison of data on the growth of population shows that the data set in advance in the transport model do not correspond to the real development over the period starting 2011.

| Planning area / region | Population |
| --- | --- |
|  | NSI | Mode |
|  | 2008 | 2011 | Growth 2011/2008 | Growth 2015/2008 |
| Northwestern | 916 054 | 836 601 | -8.67% | -4.64% |
| Northern central | 924 273 | 853 468 | -7.66% | -4.68% |
| Northeastern | 991 471 | 961 965 | -2.98% | -4.20% |
| Southern central | 1 538 142 | 1 471 107 | -4.36% | -4.29% |

Table 2	Comparison between the projected population growth for 2011 from BMPT and the actual one reported from the National 2011 census.

## 2.5	 Conclusions concerning possibilities for model update and identification of ‘bottlenecks’ on the road and railway network

As a result of a thorough analysis the Contractor made the following conclusions regarding the possibilities to update the transport models of GTMP:

- Models are not flexible with respect to changes both in the international environment for the transport sector and in the domestic one as a realization of projects or phases thereof, e.g.; They allow the update of a limited number of factors only that are indicated above. All other factors influencing the demand for transport have been adopted either as constant ones or require additional modeling. An important example in this respect is the complete impossibility to change the characteristics of freight transport services demand internationally-wise owing to a change in the economic environment in a particular country/ foreign trade partner (e.g. Greece).

- The absence of flexibility in the models means that even if data could be updated successfully, this being possible for them through the interface, the model will produce results that are irrelevant to the economic reality of present day.

- The update of input data in the model can not bring in the result the Contracting Authority needs, namely: identification of the bottlenecks. The reason for this is in the standardized pre-set form of output results at the national level only, but not at the level of a project and/or a segment of the infrastructure network.

- In order to satisfy the requirements of the Technical specification the most suitable approach is new modeling with making use, to the highest possible degree, of the models prepared within the framework of GMPT. This comprises the following steps:

- Update of the model of passenger services against a new baseline year

- Preparation of a new model of the overland freight transport against the baseline year

- Formulation of a demand on the demand for passenger services

- Formulation of a demand on the demand for freight transport

- Modeling the infrastructure networks to 2020.

- Assignment of the projected passenger and freight traffic on the respective infrastructure networks and identification of the bottlenecks.

Implementation of each of the steps and the respective results are presented in the following sections of this report.

# Selection of baseline year, system of zoning and scope of the infrastructure networks

The requirement of the Contractor for incorporation in the model of changes in ‘the commodity turnover, ….. and data about the traffic’, and also the accurate reporting of changes occurred in the economic environment both in the country and in the business partners necessitate the development of a model for a new baseline year.

The selection of a new baseline year for the transport model is of material importance, the natural strive being to a nearest possible year for which enough data is available, including social-economic and transport data. Data for 2012 are still not available and insofar as such are at hand, this is preliminary data subject to particularization.

In accordance with the requirement of the Contracting Authority to have the changes in the number, territorial distribution and age of the population reflected, as ascertained during the latest census, the Contractor proposed and the Contracting Authority accepted to adopt 2011 as a new baseline year. An additional advantage for the adoption of 2011 as a baseline year is that it follows immediately the year 2010 when the latest General Profile counting of traffic on the roads was conducted and, hence, it can be accepted with a sufficient degree of certainty that differences in the intensity of movement on the core and comprehensive road network, subject matter of the project, are minimal.

While taking into account the restrictive factors the scope of the infrastructure networks and their respective system of zoning are brought into compliance with the needs of the Contracting Authority – the core and comprehensive TEN-T network and connections thereto. The updated system of zoning consists of:

- 160 domestic zones, and

- 37 international (outside the country) zones,

shown in the following figures and maps, and in detail – in Schedules 1 and 2.

Like in the model of GTMP the system of zoning in the country is based on the smallest unit of administrative-territorial division for which the national statistics collects and publishes on a regular basis demographic and social-economic data – the municipality. Additionally, in view of achieving relatively homogenous zones from the perspective of area of the territory and population number, certain municipalities were aggregated in one zone. Sofia Metropolitan Municipality, to the contrary, it was disaggregated into 7 zones.

Fig. 3 	System of zoning, domestic zones

Fig. 4 	System of zoning, partially international zones

The length of the modeled automobile network on the territory of the country is 11 282 km and is divided into 615 sections. The total length of the modeled road network, including that out of the country and the future network by 2020 amounts to 65 617 km and 1 264 sections. Each section has been assigned the following characteristics:

- Length

- Road class

- Average speed of movement for three categories of transport vehicles:

- Passenger cars

- Coaches, and

- Cargo trucks

- Throughput

- Number of passenger cars, coaches and cargo trucks and total MTV from the General Profile counting of automobile traffic in 2005 and 2010 (for the sections in Bulgaria only, and if there is a counting point in the section).

It has to be noted that for 332 sections from the core network and part of the comprehensive one of TEN-T the Consultant changed the speed functions from the GTMP model with averaged speeds registered by GPS of a large number of MTV of up to 3.5 t, that have traveled through the respective section in 2011. The average number of MTV that served as a basis for calculation o the average speed for the respective section was around 114 thousand, which is an indicator of a high level of reliability of data. The influence has been thus accounted for of speed restrictions imposed by the RTA, as well as multiple factors and possible events occurring within the framework of the calendar  year (atmospheric, climatic, repairs and other). The average section speed for coaches and cargo trucks in these sections was adjusted in proportion to the speed for MTV of up to 3.5 t.

The model of the railway network on the territory of Bulgaria includes all lines in operation by the base year 2011 with a total length of 3 895 km, divided into 328 sections. The total length of modeled network, including out of the country, amounts to 40 582 km, divided into 930 sections. Each section has been assigned the following characteristics:

- Length

- Design speed

- Average speed of movement of trains for the transport of passengers and transport of freight

- Type of the line:

- Number of tracks (single-track/ double-track or more)

- Electrified/ non-electrified

- Conventional or high-speed

- Type of track-gauge, etc.

The following figures present the modeled road and railway networks.

Fig. 5 	Modeled road network in Bulgaria for the baseline year of 2011.

Fig. 6	Scope of the modeled railway network in Bulgaria for the baseline year 2011.

# Update of the model of passenger services against a new baseline year

The Contractor updated the synthetic model of demand for passenger services by automobile transport from the BMPT by updating the factors of generation and attraction of trips: population and generalized costs between each pair of zones by purpose of the trip.

The source of data on the population by zones to the baseline year is the 2011 Population and Housing Census in the Republic of Bulgaria.

Modeled are the interzone trips by three purposes:

- Daily trips (to/from workplace, for training)

- Business trips

- Private trips.

Daily and business trips are modeled on the grounds of the number of active population by zones, while the total population – for modeling the private trips. Presented in the following table are summarized data about the number of population by regions as at the date 01.02.2011, the date of conducting the population census.

|  | 2011 |
| --- | --- |
|  | Population | Active population |
| BULGARIA | 7 364 570 | 3 329 683 |
| Northern and Eastern Bulgaria | 3 752 349 | 1 617 969 |
| Northwestern area | 847 138 | 340 372 |
| Vidin | 101 018 | 38 269 |
| Vratsa | 186 848 | 75 643 |
| Lovech | 141 422 | 56 641 |
| Montana | 148 098 | 60 803 |
| Pleven | 269 752 | 109 016 |
| Northern central area | 861 112 | 368 189 |
| Veliko Tarnovo | 258 494 | 109 932 |
| Gabrovo | 122 702 | 55 250 |
| Razgrad | 125 190 | 52 661 |
| Ruse | 235 252 | 104 360 |
| Silistra | 119 474 | 45 986 |
| Northeastern area | 966 097 | 433 618 |
| Varna | 475 074 | 226 204 |
| Dobrich | 189 677 | 80 743 |
| Targovishte | 120 818 | 49 579 |
| Shumen | 180 528 | 77 092 |
| Southeastern area | 1 078 002 | 475 790 |
| Burgas | 415 817 | 190 714 |
| Sliven | 197 473 | 78 926 |
| Stara Zagora | 333 265 | 149 742 |
| Yambol | 131 447 | 56 408 |
| Southwestern and Southern central Bulgaria | 3 612 221 | 1 711 714 |
| Southwestern area | 2 132 848 | 1 062 620 |
| Blagoevgrad | 323 552 | 152 644 |
| Kyustendil | 136 686 | 57 470 |
| Pernik | 133 530 | 61 526 |
| Sofia | 247 489 | 110 499 |
| Sofia city | 1 291 591 | 680 481 |
| Southern central area | 1 479 373 | 649 094 |
| Kurdjali | 152 808 | 61 210 |
| Pazardjik | 275 548 | 116 415 |
| Plovdiv | 683 027 | 306 775 |
| Smolyan | 121 752 | 58 901 |
| Haskovo | 246 238 | 105 793 |

Table 3	Population by regions and planning areas by 01.02.2011.

## 4.1	Trips by passenger cars

Trips by passenger cars for the baseline 2011 were modeled by the gravity model used in GTMP, described by the following formula

,

where:

Dij is the demand for trips from the zone of origin i to the zone of destination j

Pi is the population in the zone of origin i

Aj is the population in the zone of destination j

Cij is the generalized cost of travel by passenger car from zone i to zone j,

k, (, (, ( and ( are parameters calibrated in BMPT, as shown in the table below:

| Parameters | Passenger car |
| --- | --- |
|  | Daily | Business | Private |
|  | 3.207E-07 | 3.063E-07 | 1.645E-07 |
|  | 1.000 | 1.000 | 1.000 |
|  | 1.140 | 1.140 | 1.139 |
|  | -0.038 | -0.017 | -0.013 |
|  | -0.984 | -1.070 | -1.083 |

Table 4	Calibrated parameters for obtaining matrixes of the synthetic automobile trips

Generalized costs Cij of travelling by passenger car from zone i to zone j are calculated for each pair of zones of origin and designated after the following formula:

Cij = t*V + l*p*e,

where:

t is the time in minutes for travelling from the zone of origin to the zone of destination over the road network updated for 2011

V is the price of time in €ct

l is the distance in km from the zone of origin to the zone of destination (over the updated network as well)

р is the average fuel price per liter (updated for 2011 – an average of BGN2.40 for А 95  gasoline and BGN2.46 for the diesel fuel)

е is the average fuel consumption of a passenger car per km, determined in BMPT for 2011.

In conformity with the requirements for preparing a CBA in the transport sector the price of time for 2008 used in BMPT, as shown in the table below, was updated for 2011 with an elasticity factor of 0.7 against the GDP growth per capita.

| Purpose of the trip | Price of time (€ct/min) |
| --- | --- |
|  | BMPT 2008 | 2011 |
| Daily | 7.30 | 7.12 |
| Business | 19.77 | 19.29 |
| Private | 7.30 | 7.12 |

Table 5	Values of the price of time for passenger trips for 2008 and 2011.

The drop in the price of time for the passengers in 2011 against 2008 was the result of the GDP drop from 5.5% in 2009, which was compensated only partially by the growth of 0.4% in 2010 and 1.7% in 2011.

The results thus obtained for generated daily trips by zones were compared and where necessary – adjusted against the NSI data about daily labour migrants and commuting students by municipalities and mode of transport, an extract of which is presented in the two tables below. In view of the adopted system of zoning trips within the boundaries of the same municipality are ignored.

7. Daily labour migrants by destination of migration

| Regions Municipalities | Employed persons | Persons living and working in the same inhabited location | Daily labour migrants | Daily labour migrants per 1000 employed persons |
| --- | --- | --- | --- | --- |
|  |  |  | total | of them going to work |  |
|  |  |  |  | in the same municipality | in a municipality of the same region | in a municipality of another region |  |
|  |  |  |  | in cities | in villages | in cities | in villages | in cities | in villages |  |
|  | number |  |
| Total for the country | 2834834 | 2434511 | 400323 | 98805 | 47801 | 116045 | 33409 | 93337 | 10926 | 141.2 |
| Blagoevgrad | 127583 | 106464 | 21119 | 7538 | 3675 | 6404 | 1225 | 2115 | 162 | 165.5 |
| Bansko | 5830 | 5018 | 812 | 497 | 37 | 173 | 17 | 71 | 17 | 139.3 |
| Belitsa | 2593 | 1694 | 899 | 185 | 49 | 551 | .. | 70 | .. | 346.7 |
| Blagoevgrad | 33064 | 30533 | 2531 | 957 | 187 | 346 | 122 | 823 | 96 | 76.5 |
| Gotse Delchev | 13376 | 11646 | 1730 | 1011 | 151 | 193 | 197 | 169 | 9 | 129.3 |
| Gurmen | 5204 | 3484 | 1720 | - | 310 | 1236 | 114 | 59 | .. | 330.5 |
| Kresna | 1930 | 1439 | 491 | 148 | 51 | 173 | 71 | 48 | - | 254.4 |
| Petrich | 21816 | 17918 | 3898 | 1884 | 1425 | 315 | 91 | 172 | 11 | 178.7 |
| Razlog | 8243 | 6082 | 2161 | 878 | 75 | 1097 | 13 | 93 | 5 | 262.2 |
| Sandansky | 16536 | 13653 | 2883 | 1436 | 593 | 318 | 369 | 161 | 6 | 174.3 |
| Satovcha | 5323 | 4761 | 562 | - | 306 | 91 | .. | 101 | .. | 105.6 |
| Simitli | 4475 | 3123 | 1352 | 251 | 154 | 786 | 25 | 131 | 5 | 302.1 |
| Strumyani | 1499 | 902 | 597 | - | 208 | 301 | 58 | 30 | - | 398.3 |
| Hadjidimovo | 4216 | 3356 | 860 | 180 | 95 | 514 | .. | 37 | .. | 204.0 |
| Yakoruda | 3478 | 2855 | 623 | 111 | 34 | 310 | 10 | 150 | 8 | 179.1 |

7. Daily labour migrants by place of residence, sex, mode of transport used and destination of migration

| Place of residence Sex Mode of transport | Daily labour migrants |
| --- | --- |
|  | total | of them going to work |
|  |  | within the same region | in other regions |
|  |  | total | In cities | In villages | total | In cities | In villages |
| Total | 400323 | 296060 | 214850 | 81210 | 104263 | 93337 | 10926 |
| No daily traveling | 30036 | 10700 | 7939 | 2761 | 19336 | 17960 | 1376 |
| Passenger car | 152720 | 115203 | 86802 | 28401 | 37517 | 33856 | 3661 |
| Train | 21437 | 9832 | 7861 | 1971 | 11605 | 11076 | 529 |
| Coach/minibus | 188970 | 155359 | 109130 | 46229 | 33611 | 28421 | 5190 |
| Motorcycle | 354 | 305 | 195 | 110 | 49 | 40 | 9 |
| Bicycle | 1501 | 1368 | 841 | 527 | 133 | 110 | 23 |
| Other | 5305 | 3293 | 2082 | 1211 | 2012 | 1874 | 138 |

Table 6	An example of NSI data for the daily labour trips

International trips by passenger car were estimated on the basis of NSI data for travels of Bulgarian citizens abroad by countries and purpose of the trip, and visits of foreigners to Bulgaria by purpose of the trip and by countries for 2011, as presented in Schedules 3 and 4. This data was adjusted with the number of trips by air transport by airports.

The resultant asymmetric matrixs by purpose of trip were normalized in order to obtain a symmetric matrix in which the number of outbound trips from a particular zone is equal to the number of inbound trips.

With the help of factors for medium occupancy of a passenger car (1.7885 for daily trips, 1.7681 for business and 2.2854 for private trips) depending on the purpose of the trip, the matrixes in passengers were transformed into matrixes in passenger cars (average 24-hour number of trips by passenger car). The resultant matrixes were assigned on the road network model in PTV VISUM environment and compared with the average 24-hour intensity of automobile traffic by sections of the national roads for 2011 (117 main counting points) or for 2010 (additional counting points). On the basis of such results the matrixes were specified by way of iteration. The ultimate result from validation of the matrix of domestic passenger trips by passenger car is presented in the graph below. The Consultant’s main objective in the process of specifying the matrixes is to achieve maximum possible accuracy along the sections of the core and the comprehensive TEN-T network.

Fig. 7	Comparison between modeled and registered intensity of passenger car traffic for the baseline 2011.

Summarized data on trips by passenger cars are presented in the following table:

|  | Average 24-hour number f trips by passenger car for 2011 |
| --- | --- |
|  | Total | Daily | Business | Private |
| Domestic trips | 405 173 | 85 888 | 47 664 | 271 621 |
| International trips | 39 013 |  | 7 920 | 31 093 |
| Outbound | 16 538 |  | 3 960 | 12 578 |
| Inbound | 16 538 |  | 3 960 | 12 578 |
| Transit | 5 937 |  |  | 5 937 |
| TOTAL | 444 186 | 85 888 | 55 584 | 302 714 |

Table 7	Estimated average 24-hour number of interzone trips by passenger car for the baseline year 2011.

The maps here below visualize the main characteristics of demand for trips by passenger car in 2011.

Fig. 8	The 50 destinations with busiest traffic for daily interzone trips by passenger car

Fig. 9	The 50 destinations with busiest traffic for business interzone trips by passenger car

Fig. 10	The 50 destinations with busiest traffic for private interzone trips by passenger car

## 4.2	Coach transport services

The matrix of coach transport services was updated in two steps:

- by way of updating a model of the coach ‘network’ from BMPT, which represents, by essence, the timetables of intercity coach lines by the baseline year 2008, with the data valid by 2011.

- adjusting the results against NSI data for the daily trips of labour migrants and students represented here above and respectively, by specifying the balance under the other two purposes – business and private.

According to data from the Automobile Administration EA that was processed by the Consultant and used in the update, the sum of the average 24-hour interzone matrix of coach lines only from the National transport scheme is 4 800. When this matrix was assigned on the network the Consultant found that along the core and additional ТЕN-Т network assigned traffic considerable exceeded the actually counted one, which, besides such lines also includes incidental coach services as a minimum. For such reason the matrix was adjusted by excluding a vast number of lines over duplicating routes and the final sum of the matrix of regular lines amounted to 2 312. This corresponds to the number of lines maintained under timetable in 2011 – 2 794, as per NSI data.

The average 24-hour number of domestic trips by coach was estimated on the basis of an assumed coach occupancy by 35 passengers and distributed by purpose of the trip firstly, based on the data of NSI for daily trips, and the balance – in accordance with the relative shares of business and private trips, as specified in GTMP.

International trips by coach transport were updated on the grounds of the NSI data indicated above for trips of Bulgarian citizens abroad and visits of foreigners to Bulgaria.

Used in GTMP are data for 2006 about number of passengers and for 2003 on the number of MTV passed through BCP. Such data is not available any more and for such reason modeled traffic is validated by using data from the counting points closest to the borders along the National Road Network.

Summarized data about a finally specified matrix of trips by coach is presented in the table below.

|  | Total |
| --- | --- |
| Domestic trips | 80 936 |
| International trips | 20 152 |
| Outbound | 7 920 |
| Inbound | 7 920 |
| Transit | 4 312 |
| Total | 101 088 |

Table 8	Estimated average 24-hour number of interzone trips by coach for the baseline year 2011.

The following map visualizes the main characteristics of demand for coach trips in 2011.

A summarization is presented on Figure 11 for the average 24-hour number of passenger trips by automobile transport (passenger car and coach) by sections of the National Road Network.

Fig. 11	The 50 busiest destinations with interzone coach services

Fig. 12	Average 24-hour number of passengers in 2011 by sections of the road network (by passenger car and coach)

## 4.3	Railway transport services

Update of trips by rail in 2011 was made on the basis of two main sources of information:

- Number of carried passengers by stations and

- Yearly matrixes for number of passengers on accelerated fast trains, fast trains and passenger trains, produced within the framework of the Evaluation of market demand for railway transport passenger services in the Republic of Bulgaria and elaboration of measures for their optimization, project financed under the OP on Transport and implemented by consortium InfraCare - TransCare.

The total number of carried passengers in 2011 was 29.3 mill., of which:

- With tickets – 7.2 mill., 388 thou. of which in international destinations

- With cards under contracts – 7.2 mill.

- Other – 0.02 mill.

Stations with more than 100 000 passengers for 2011 are presented in the following figure 13.

Matrixes from the survey for Evaluation of market demand for railway transport passenger services in the Republic of Bulgaria and elaboration of measures for their optimization are at the regional level (27х27) and they refer to the first 8 months of 2012. For this reasons they were extended to the full value of carried passengers for 2011. The matrixes were additionally distributed at a zone level on the basis of number of passengers carried by stations that are located on the territory of the respective zone.

The produced yearly matrixes were assigned on the model of the railway network and the results – compared with the number of trains by sections. The resultant medium occupancy of trains along destinations of the core and comprehensive TEN-T network was juxtaposed with data about train occupancy by market segments and the respective matrixes were adjusted, where necessary.

The maps below visualize the main characteristics of demand for railway transport services in 2011. Data was summarized at the national level in the following table.

|  | Average 24-hour trips by railway for 2011 |
| --- | --- |
|  | Total | Accelerated fast | Fast | Passenger |
| Domestic trips | 72 666 | 3 595 | 19 275 | 49 796 |
| International trips | 1 063 | 1 063 |  |
| TOTAL | 73 729 | 23 933 | 49 796 |

Table 9	Estimated average 24-hour number of trips by railway

Fig. 13	Stations with more than 100 000 passengers for 2011.

Fig. 14	The 25 busiest destinations for interzone trips on accelerated fast trains

Fig. 15	The 25 busiest destinations for interzone trips on fast trains

Fig. 16	The 50 busiest destinations for interzone trips on passenger trains

Fig. 17	Passengers carried by railway transport in 2011 on sections of the railway network

## 4.4	Conclusions about demand for passenger services in 2011

The estimated average 24-hour number of interzone passenger trips and their distribution by mode of transport and market segments for the baseline year 2011 is presented in the following table and figure.

|  | Average 24-hour number of interzone passenger trips in 2011 |
| --- | --- |
|  | Domestic | share | International | share | Total | share |
| Passenger car | 405 173 | 72.5% | 39 013 | 64.8% | 444 186 | 71.8% |
| Coach | 80 936 | 14.5% | 20 152 | 33.5% | 101 088 | 16.3% |
| Railway | 72 666 | 13.0% | 1 063 | 1.8% | 73 729 | 11.9% |
| Total | 558 775 | 100.0% | 60 227 | 100.0% | 619 003 | 100.0% |

Table 10	Distribution of demand for passenger services by mode of transport and market segments for the baseline 2011.

Fig. 18	Distribution of passenger trips in 2011 by mode of transport (public and individual)

## 4.5	Freight services by automobile transport

As specified in it. 3.1 BMFT was developed in an environment of electronic tables that are not part of the files connected with the update procedure described in it. 3.4. This necessitated, in fact, a completely new modeling of matrixes for the baseline year 2011.

### 4.5.1	Domestic freight transport

The main source of information about the modeling of domestic freight services was the study by NSI of the freight automobile transport that is conducted annually and in accordance with the requirements of Regulation 1172/98 of EEC. Included in the survey are cargo automobiles – trucks, special automobiles that, in accordance with their function, perform carriage of freight and tractors with Bulgarian registration and total weight above 6 t.

Used in the modeling of the matrix for the baseline year are detailed data about:

- Domestic services total (for own account and for consideration) of the freight automobile transport by 20 groups of commodities from the NCNT and region of loading in t and tkm; and

- Domestic services total (for own account and for consideration) of the freight automobile transport by 20 groups of commodities from the NCNT and region of unloading in t and tkm.

In order to ensure comparability with data on the other modes of transport the Consultant reduced the freight to the 10 commodity groups that are used in forecasts at the European level of the EC Mobility and Transport DG, presented in the following table.

| Commodity groups | Domestic services by automobile transport 2011, thou. t |
| --- | --- |
| 0 | Agricultural products and livestock | 12 430 |
| 1 | Food products and fodder | 7 395 |
| 2 | Solid mineral substances | 1 109 |
| 3 | Oil and oil products | 4 301 |
| 4 | Ore and metal scrap | 2 001 |
| 5 | Products of the ferrous and non-ferrous metallurgy | 1 615 |
| 6 | Processed and unprocessed mineral resources and minerals, building products | 59 729 |
| 7 | Fertilizers | 641 |
| 8 | Chemical substances and products | 7 649 |
| 9 | Machines, means of transport, manufactured goods and variety of other commodities | 23 809 |
| Total | 120 635 |

Table 11	Freight carried by automobile transport in 2011 under domestic services by commodity groups.

The distribution of generated (loaded) and attracted (offloaded) freight in a particular region was made on the basis of economic and demographic characteristics of the zones within the framework of each region: total population, active population, production facilities and sources of raw materials (mines, quarries, etc.). The intrazone transport was estimated at 15.9 mill. t.

It was estimated by NSI data about freight automobile transport by total weight of the means of transport that the average loading of a cargo automobile on a full trip under domestic service is 15.8 t. With a 54% share of the run without load under domestic service the resultant average freight on a means of transport registered along the network is 7.2 t. The summary matrix of freight carried on domestic services was transformed into a matrix of the average 24-hour number of cargo automobiles, which was assigned on the automobile network model and specified on the grounds of a comparison with the actually counted number of cargo automobiles by sections.

### 4.5.2	Import and export by automobile transport

The consultant produced matrixes for the import and export of goods by automobile transport in 2011 on the basis of data from the NSI statistical study on the movement of goods from/to Bulgaria. The main sources of information for this study are:

- Intrastat declarations for arrivals and forwarding of goods from/to member-countries of the EU;

- The unified administrative documents that is completed by all entities performing import or export of goods from/to third countries.

The NSI aggregated data contain information about the state from/to which the freight is designated, the type of freight after the Harmonized System (HS), the quantity in kg, the form of transport, etc. Thus in reality, the Consultant only transforms the type of freight from HS into the nomenclature  of freight presented here above and aggregates the data in conformity with the adopted system of zoning out of the country.

### 4.5.3	Transit automobile transport

Very much like the import and export the matrixes for transit automobile transport are also produced on the basis of data from NSI and the Customs Agency about the gross weight of goods carried by automobile transport through the territory of the country from a dispatch to a receiving customs office.

### 4.5.4	Interzone freight services by automobile transport

The estimation on the interzone carriage of freight in 2011 by automobile transport is presented in the table below.

| Type of services | mill. t |
| --- | --- |
| Domestic, incl. | 120.6 |
| Intrazone | 15.9 |
| Interzone | 104.7 |
| International, incl.: | 46.5 |
| Import | 21.2 |
| Export | 17.1 |
| Transit | 8.3 |
| TOTAL | 167.2 |

Table 12	Freight services by automobile transport in 2011 by market segments

The result of assigning the matrixes of domestic and international carriage in tons to the model of the automobile network is presented in the following Fig. 19.

According to NSI data on the freight automobile transport by total weight of the means of transport it was estimated that the average loading of a cargo truck in the case of a complete trip over an international service was 18.8 t. Compared against domestic services the relative share of empty legs under international ones is very low – 12.7%. Based on this data the Consultant judged that the average loading of a cargo truck under international services is 16.2 t. The summary matrix of import, export and transit freight in tons carried by automobile transport in 2011 was transformed into a matrix of the average 24-hour number of cargo automobiles.

Fig. 19	Freight carried by automobile transport in 2011 by sections of the road network

## 4.6	Freight services by railway transport

The matrixes for freight services by railway transport for the baseline year 2011 were produced by aggregation at zone level of records for carriage from loading station to offloading station obtained from ‘Railway Transport’ EA. Additionally, the Consultant brought the data forwarded into compliance with the nomenclature of freight presented here above in it. 4.5.1. The data is summarized in the following tables:

| Type of services | mill. t |
| --- | --- |
| Domestic | 11.960 |
| International, incl.: | 1.196 |
| Import | 0.954 |
| Export | 1.438 |
| Transit | 3.588 |
| TOTAL | 15.547 |

Table 13	Freight services by railway transport in 2011 by market segments

| Commodity groups | Domestic services by railway transport 2011, thou. t |
| --- | --- |
| 0 | Agricultural products and livestock | 427 |
| 1 | Food products and fodder | 150 |
| 2 | Solid mineral substances | 3 953 |
| 3 | Oil and oil products | 1 911 |
| 4 | Ore and metal scrap | 2 963 |
| 5 | Products of the ferrous and non-ferrous metallurgy | 1 246 |
| 6 | Processed and unprocessed mineral resources and minerals, building products | 270 |
| 7 | Fertilizers | 0 |
| 8 | Chemical substances and products | 1 801 |
| 9 | Machines, means of transport, manufactured goods and variety of other commodities | 2 828 |
| Total | 15 547 |

Table 14	Freight carried by railway transport in 2011 by commodity groups

The result of the assignment of the summary matrix of freight transport by railway in tons to the model of the railway network is presented in the following Fig. 20.

Fig. 20	Freight carried by railway transport in 2011 by sections of the railway network

## 4.7	Conclusions on demand for freight services in 2011

The distribution of freight carried in 2011, by commodity groups and mode of transport is presented in the table below.

| Commodity group | Automobile | Railway |
| --- | --- | --- |
|  | thou. t | share | thou. t | share |
| 0 | Agricultural products and livestock | 16 819 | 97.5% | 427 | 2.5% |
| 1 | Food products and fodder | 10 250 | 98.6% | 150 | 1.4% |
| 2 | Solid mineral substances | 4 250 | 51.8% | 3 953 | 48.2% |
| 3 | Oil and oil products | 13 869 | 87.9% | 1 911 | 12.1% |
| 4 | Ore and metal scrap | 2 584 | 46.6% | 2 963 | 53.4% |
| 5 | Products of the ferrous and non-ferrous metallurgy | 6 302 | 83.5% | 1 246 | 16.5% |
| 6 | Processed and unprocessed mineral resources and minerals, building products | 56 460 | 99.5% | 270 | 0.5% |
| 7 | Fertilizers | 2 370 | 100.0% | 0 | 0.0% |
| 8 | Chemical substances and products | 10 070 | 84.8% | 1 801 | 15.2% |
| 9 | Machines, means of transport, manufactured goods and variety of other commodities | 28 245 | 90.9% | 2 828 | 9.1% |
|  | TOTAL | 151 219 | 90.7% | 15 547 | 9.3% |

Table 15	Distribution of demand for interzone freight transport services by commodity groups and mode of transport for the baseline 2011.

The distribution of demand for freight services by mode of transport at regional level is visualized in the following figure 21.

Fig. 21	Distribution of demand for freight transport services in 2011 by mode of transport (automobile and railway)

## 4.8	Passenger and freight traffic on the road network

Modeling the demand for transport services for the baseline year 2011 ended with the assignment of summary matrixes for average 24-hour number of passenger, cargo automobiles and coaches to the model of the road network by 2011.

It can be seen in the graph below that the modeled automobile traffic (total MTV) assigned on the network displays a high level of correlation (R2 = 0.81) with the registered one from the profile counts of automobile traffic.

Fig. 22	Comparison between modeled and registered intensity of MTV traffic for the baseline 2011.

A cartogram of the average 24-hour yearly intensity by sections of the NRN is shown in the figure below.

Fig. 23	Average 24-hour intensity of interzone automobile traffic on the NRN for 2011.

# Update of forecasts on factors influencing the demand for passenger services

According to BMPT of GTMP ‘the factors,…, that have a potential of significant influence on the forecasting of growth are as follows::

- Economic growth – change in the GDP per capita examined at regional level as an indicator of household income (as recommended in the Requirements for the elaboration of cost-benefits analysis in Bulgaria)

- Change in the population and employment – the change in the population and the employment are considered at the regional level

- Ownership of passenger cars – Change in the ownership of passenger (automobiles per 1 000 residents)

- Monetary value of time – Change in the values of time in accordance with the purpose of the trip of individual travelers in Bulgaria, in conformity with the instructions in Requirements for  the elaboration of a Cost-benefits analysis for the transport sector in Bulgaria

- Change in the monetary value of travel – Change in the consumption of fuel per km, which reflects an improvement in the engine efficiency of the means of transport, based on the EC guidelines, and

- Change in the price of services in public transport – change in the prices of public transport paid by the passengers.’

In accordance with the above the Consultant updated the forecasts for factors as presented here below.

## Forecast on the growth in GDP

The Consultant updated the forecast on Bulgaria’s economic development on the basis of two sources of information:

- Medium-term demand on 2014 - 2016, approved by the Government, presented in the following table, and

- recommended values of the real annual growth in GDP after 2016 – 3.3%.

|  | Budget 2013 | Revised data 2013 | 2014 | 2015 | 2016 |
| --- | --- | --- | --- | --- | --- |
| GDP, bill. Levs | 81.485 | 79.932 | 83.315 | 87.589 | 92.583 |
| Economic growth | 1.9% | 1.0% | 1.8% | 2.9% | 3.4% |

Table 16	Growth in the GDP, in accordance with the medium-term demand on 2014 - 2016 of the government

The accumulated growth in GDP, in accordance with the updated forecast is presented in the following table.

| Period | Real yearly growth in GDP |
| --- | --- |
| 2012 – 2013 | 0.80% |
| 2013 - 2014 | 1.00% |
| 2014 - 2015 | 1.80% |
| 2015 - 2016 | 2.90% |
| 2016 - 2017 | 3.40% |
| 2017 - 2020 | 3.30% |
| 2020 - 2030 | 3.30% |
| Accumulated growth (2011 - 2020) | +25.56% |
| Accumulated growth (2011 - 2030) | +73.73% |

Table 17	Summarization of the updated forecast for growth in GDP at the national level

Based on the updated forecast at the national level and projections for growth in the GDP by regions from GTMP the Consultant updated the forecast by regions and planning areas, as presented in the diagrams below. In conformity with the BMPT methodology it was assumed that a growth in GDP at zone level will be equal to the projected increase at the levels of district / region.

Accumulated growth in GDP by 2020, 2011 = 100%

Northwestern    Northern Central  Northeastern   Sofia      Blagoevgrad   Southwestern   Central Southern  St. Zagora  Southeastern  Bulgaria

Planned	Updated

Accumulated growth in GDP by 2030, 2011 = 100%

Northwestern    Northern Central  Northeastern   Sofia      Blagoevgrad   Southwestern   Central Southern  St. Zagora  Southeastern  Bulgaria

Planned	Updated

Fig. 24	Comparison between the GDP growth projected in GTMP and the updated one

As evident from the above diagrams for all regions the updated demand on growth in GDP lags behind against the one from GTMP by 13 to 33 percentage points for 2020 and, respectively, by 26 to 58 points for 2030.

Northwestern   Northern Central   Northeastern   Sofia       Blagoevgrad  Southwestern   Central Southern  St. Zagora  Southeastern  Bulgaria

Fig. 25	Backlog in the updated GDP growth by districts / regions against the forecast from GTMP

According to the growth models in BMPT and BMFT the lag in the projected GDP growth affects negatively the demand for passenger transport services. The same directly proportional dependence exists also between the growth in GDP and the demand for freight services.

## 5.2	Demographic forecast

The Consultant updated the demand on population growth at regional level on the basis the NSI forecast under a convergence hypothesis that is defined as a realistic one and conforms to the statutory requirements of the European Union to the demographic and social-economic development of the member countries. According to the current forecast until 2030 the population of this country will be decreasing, on the average, by 0.6% annually (against the population by 31.12.2011).

According to the BMPT methodology the drop in the total population and in the number of active population will render a negative influence on the demand for passenger services as it is accepted that ‘demand is in linear proportion to population, sо that a 5% drop in the population means a 5% drop in trips. In the forecast model:

- The active population (as an approximate indicator of employment, which is not available at the national level) is used for daily trips and business trips, and

- the total population is used for leisure trips.’

Detailed data about the total population and the number of active population at regional level is presented in the following two tables.

| POPULATION | 2011 | 2020 | 2030 | Increase against 2011 |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2020 | 2030 |
| BULGARIA | 7 364 570 | 6 950 436 | 6 519 217 | -6% | -11% |
| Northern and Eastern Bulgaria | 3 752 349 | 3 462 007 | 3 179 676 | -8% | -15% |
| Northwestern area | 847 138 | 742 587 | 655 597 | -12% | -23% |
| Vidin | 101 018 | 86 054 | 74 416 | -15% | -26% |
| Vratsa | 186 848 | 164 997 | 146 471 | -12% | -22% |
| Lovech | 141 422 | 123 385 | 108 227 | -13% | -23% |
| Montana | 148 098 | 127 995 | 112 145 | -14% | -24% |
| Pleven | 269 752 | 240 156 | 214 338 | -11% | -21% |
| Northern central area | 861 112 | 779 952 | 701 539 | -9% | -19% |
| Veliko Tarnovo | 258 494 | 236 400 | 214 939 | -9% | -17% |
| Gabrovo | 122 702 | 108 446 | 94 597 | -12% | -23% |
| Razgrad | 125 190 | 108 590 | 93 291 | -13% | -25% |
| Ruse | 235 252 | 218 241 | 201 680 | -7% | -14% |
| Silistra | 119 474 | 108 275 | 97 032 | -9% | -19% |
| Northeastern area | 966 097 | 919 695 | 863 735 | -5% | -11% |
| Varna | 475 074 | 466 663 | 448 633 | -2% | -6% |
| Dobrich | 189 677 | 172 398 | 155 691 | -9% | -18% |
| Targovishte | 120 818 | 110 642 | 101 250 | -8% | -16% |
| Shumen | 180 528 | 169 992 | 158 161 | -6% | -12% |
| Southeastern area | 1 078 002 | 1 019 773 | 958 805 | -5% | -11% |
| Burgas | 415 817 | 404 313 | 388 534 | -3% | -7% |
| Sliven | 197 473 | 188 497 | 180 323 | -5% | -9% |
| Stara Zagora | 333 265 | 309 749 | 285 203 | -7% | -14% |
| Yambol | 131 447 | 117 214 | 104 745 | -11% | -20% |
| Southwestern and Southern central Bulgaria | 3 612 221 | 3 488 429 | 3 339 541 | -3% | -8% |
| Southwestern area | 2 132 848 | 2 104 653 | 2 060 331 | -1% | -3% |
| Blagoevgrad | 323 552 | 305 695 | 282 310 | -6% | -13% |
| Kyustendil | 136 686 | 118 849 | 102 559 | -13% | -25% |
| Pernik | 133 530 | 117 213 | 101 852 | -12% | -24% |
| Sofia | 247 489 | 227 996 | 209 051 | -8% | -16% |
| Sofia city | 1 291 591 | 1 334 900 | 1 364 559 | 3% | 6% |
| Southern central area | 1 479 373 | 1 383 776 | 1 279 210 | -6% | -14% |
| Kurdjali | 152 808 | 142 997 | 131 013 | -6% | -14% |
| Pazardjik | 275 548 | 256 121 | 235 658 | -7% | -14% |
| Plovdiv | 683 027 | 655 549 | 622 175 | -4% | -9% |
| Smolyan | 121 752 | 107 823 | 92 840 | -11% | -24% |
| Haskovo | 246 238 | 221 286 | 197 524 | -10% | -20% |

Table 18	Forecast on the population by regions and planning areas

According to the forecast used in BMPT from GTMP, it is expected that the total population in 2030 will be by 11.3% less compared against 2008, i.e. there is no significant difference in the relative indicators against the NSI forecast. In absolute values, however, the difference is a considerable one:

- According to the forecast from BMPT by 2030 the total population is 6.881 million at the national level.

- According to the NSI forecast updated after the National 2011 census, the total number by 2030 will be 6.519 mill., which is by 392 thou. people less.

Even more negative is the forecast for the number of the active population:

- According to BMPT it is expected until 2030 to decrease by 12% against 2008 and to become 3.199 mill. people

- According to the current NSI forecast at the national level the decrease for 2030 against 2011 will be 19% and the active population will count 2.712 mill. people, or by 486 thou. less.

| ACTIVE POPULATION | 2011 | 2020 | 2030 | Increase against 2011 |
| --- | --- | --- | --- | --- |
|  |  |  |  | 2020 | 2030 |
| BULGARIA | 3 329 683 | 2 940 040 | 2 712 238 | -12% | -19% |
| Northern and Eastern Bulgaria | 1 617 969 | 1 393 053 | 1 250 689 | -14% | -23% |
| Northwestern area | 340 372 | 279 179 | 239 664 | -18% | -30% |
| Vidin | 38 269 | 30 537 | 26 308 | -20% | -31% |
| Vratsa | 75 643 | 62 981 | 53 806 | -17% | -29% |
| Lovech | 56 641 | 46 280 | 39 317 | -18% | -31% |
| Montana | 60 803 | 49 430 | 42 156 | -19% | -31% |
| Pleven | 109 016 | 89 951 | 78 076 | -17% | -28% |
| Northern central area | 368 189 | 308 441 | 269 805 | -16% | -27% |
| Veliko Tarnovo | 109 932 | 91 907 | 81 758 | -16% | -26% |
| Gabrovo | 55 250 | 43 991 | 37 274 | -20% | -33% |
| Razgrad | 52 661 | 42 578 | 34 572 | -19% | -34% |
| Ruse | 104 360 | 91 395 | 82 996 | -12% | -20% |
| Silistra | 45 986 | 38 571 | 33 205 | -16% | -28% |
| Northeastern area | 433 618 | 384 985 | 355 579 | -11% | -18% |
| Varna | 226 204 | 206 963 | 198 487 | -9% | -12% |
| Dobrich | 80 743 | 67 522 | 58 791 | -16% | -27% |
| Targovishte | 49 579 | 42 449 | 37 140 | -14% | -25% |
| Shumen | 77 092 | 68 051 | 61 160 | -12% | -21% |
| Southeastern area | 475 790 | 420 448 | 385 641 | -12% | -19% |
| Burgas | 190 714 | 174 433 | 164 628 | -9% | -14% |
| Sliven | 78 926 | 70 363 | 65 264 | -11% | -17% |
| Stara Zagora | 149 742 | 129 137 | 115 746 | -14% | -23% |
| Yambol | 56 408 | 46 514 | 40 002 | -18% | -29% |
| Southwestern and Southern central Bulgaria | 1 711 714 | 1 546 987 | 1 461 549 | -10% | -15% |
| Southwestern area | 1 062 620 | 979 191 | 957 271 | -8% | -10% |
| Blagoevgrad | 152 644 | 134 723 | 118 704 | -12% | -22% |
| Kyustendil | 57 470 | 45 875 | 37 635 | -20% | -35% |
| Pernik | 61 526 | 50 241 | 41 612 | -18% | -32% |
| Sofia | 110 499 | 96 030 | 84 946 | -13% | -23% |
| Sofia city | 680 481 | 652 321 | 674 374 | -4% | -1% |
| Southern central area | 649 094 | 567 796 | 504 278 | -13% | -22% |
| Kurdjali | 61 210 | 53 813 | 46 645 | -12% | -24% |
| Pazardjik | 116 415 | 101 759 | 88 936 | -13% | -24% |
| Plovdiv | 306 775 | 275 894 | 256 031 | -10% | -17% |
| Smolyan | 58 901 | 47 625 | 36 949 | -19% | -37% |
| Haskovo | 105 793 | 88 705 | 75 715 | -16% | -28% |

Table 19	Forecast on the number of active population by regions and planning areas

## 5.3	Degree of motorization

The Consultant updated the forecast for the growth in motorization by regions (in number of passenger cars per 1 000 residents) with the help of the model for passenger car ownership from BMPT БМПТ and on the basis of the updated:

- Degree of motorization by the baseline year 2011: by NSI data the number of registered passenger cars is 2 694 821, which corresponds to a degree of motorization of 365.9 PC/
1 000 residents,

- Forecast for GDP growth

- Forecast for the population.

The summarized forecast for the degree of motorization at the national level is presented in the following table.

| Year | Number of PC/1 000 residents | Growth against 2011 |
| --- | --- | --- |
| 2011 | 365.9 |  |
| 2020 | 405.8 | +10.9% |
| 2030 | 460.9 | +26.0% |

Table 20	Update forecast for the degree of motorization

The updated forecast for degree of motorization, which is considerable ahead of the forecast from BMPT of GTMP has a positive influence on the growth in trips by passenger car and, respectively – a negative influence on the growth in demand for passenger services by public transport.

## 5.4	Price of time

In accordance with the requirements for making a CBA in the transport sector the Consultant updated the forecast for price of time for 2020 and 2030 by an elasticity factor of 0.7 against the updated growth in GDP per capita. The results are shown in the table below:

|  | Baseline year 2011 | Forecasts |
| --- | --- | --- |
|  |  | 2020 | 2030 |
| Business trips (BGN/h) | 23.57 | 29.25 | 40.95 |
| Private trips (BGN/h) | 8.70 | 10.80 | 15.11 |
| Freight (BGN/t/h) | 1.50 | 1.86 | 2.60 |

Table 21	Updated forecast for the price of time by purpose of the trip

In accordance with the updated forecasts for growth in GDP and in the population, the estimated price of time for future years is lower compared against that of BMPT. The lower price of time reduces the generalized costs. The lower sensitivity of passengers towards time of travel is usually in favour of the trips by public transport, these being traditionally connected with waiting, time of access to and from passenger terminals, time for transshipment, etc.

## 5.5	Transport costs

The Consultant updated the fuel price to the new baseline year 2011 and respectively – the forecast one for 2020 and 2030, which is more unfavourable compared to that of BMPT: it is expected that the price of fuel by 2030 will be by 27% higher than the one assumed in GTMP. This indicator has a retaining effect both on population’s mobility and on the demand for freight transport services.

The Consultant kept unchanged the forecast from BMPT for efficiency of means of transport expressed as fuel consumption per 100 km/run of a passenger car, as this indicator depends on the technological development at European and world level and has no relation to the social-economic changes in Bulgaria.

The Consultant also updated the prices of public passenger transport (railway and coach) by 2011 and on this basis the projection levels were recalculated, while preserving the trends of future development from BMPT: ‘The impact on coach and railway prices will be mainly from the increase in costs of labour, owing to the general increase in real incomes, and there is a larger percentage of costs of direct labour in the coach transport, it could be considered that under the conditions of a free market coach prices will see a higher increase than the railway ones. ….. By following this provision is made for an increase in prices within real terms both for the bus and the railway service of approximately 1% per year from 2015 to 2020.’

## 5.6	Summary of the input data for projection models

The following table summarizes the input data for projection models for demand for passenger services.

|  | Baseline year 2011 | Forecasts |
| --- | --- | --- |
|  |  | 2020 | 2030 |
| Economic factors |  |  |  |
| GDP | 75 265 300 | 25.6% | 73.7% |
| GDP per capita (BGN) | 10 220 | 13 597 | 20 057 |
|  |  | 33.0% | 96.3% |
| Demographic factors |  |  |  |
| Total population | 7 364 570 | 6 950 436 | 6 519 217 |
|  |  | -5.6% | -11.5% |
| Active population | 3 329 683 | 2 940 040 | 2 712 238 |
|  |  | -11.7% | -18.5% |
| Transport costs |
| Fuel (BGN/l) | 2.43 | 2.76 | 3.06 |
| Efficiency of PC (l/100 km) | 6.87 | 5.46 | 3.86 |
| Prices of public transport |  |  |  |
| Railway (BGN/km) | 0.0647 | 0.0798 | 0.0751 |
| Coach (BGN/km) | 0.1150 | 0.1384 | 0.1852 |
| Motorization |
| Ownership of transport vehicles (No. of passenger cars/1000 residents) | 365.9 | 405.8 | 460.9 |
| Price of time |
| Business trips (BGN/h) | 23.57 | 29.25 | 40.95 |
| Private trips (BGN/h) | 8.70 | 10.80 | 15.11 |
| Freight (BGN/t) | 1.50 | 1.86 | 2.60 |

Table 22	Summarization of input data for the forecast models

# Forecast on the demand for passenger services

For each individual zone the Consultant calculated the increase in the total number of trips generated therein regardless of the form of transport in accordance with the methodology of BMPT:

TotPaxkmpp=19.588 GDPpc0.556 +12.477 CarOwn+249.602 ,

where:

TotPaxkmpp is the total distance in km, traveled by 1 passenger in the course of 1 year (by passenger car, coach or cargo automobile)

GDPpc is the GDP per capita

CarOwn is the degree of motorization in PC /1 000 residents.

A summary of the forecast on the future demand is presented in table below. As evident, the drop in active population at zone level results in a smaller number of daily and business trips. The growth in motorization compensates only partially the effect from the decreased active population, with the average growth in daily and business trips in 2020 being negative. Negative demographic processes continue to get deeper by 2030 in most of the zones, yet the growth in motorization compensates to a much higher degree the negative trends and the average growth is a positive one.

One can observe by 2020 a modest growth of 4% on the average in the private trips against 2011. As a result of the increase in GDP and the degree of motorization the number of private trips increases  by more than 11% by 2030 against 2011.

| Purpose of trips | 2020 growth against 2011 | 2030 growth against 2011 |
| --- | --- | --- |
|  | Min | Max | Средно | Min | Max | Средно |
| Daily | -8.5% | +4.6% | -3.1% | -10.9% | +24.6% | +0.3% |
| Business | -8.5% | +4.6% | -3.1% | -10.9% | +24.6% | +0.3% |
| Private | -1.0% | +12.8% | +4.0% | 0.0% | 32.8% | 11.1% |

Table 23	Variations of growth in the generated passenger trips by zones

At a next step and in conformity with the methodology of BMPT the Consultant produced the distribution of trips by individual (passenger automobile) and public (by coach or train) form of transport:

CarPaxkmpp=10.427 GDPpc0.595 +11.603 CarOwn – 518.718 ,

where:

CarPaxkmpp is the total distance in km, traveled by 1 passenger in the course of 1 year by passenger car

GDPpc is the GDP per capita

CarOwn is the degree of motorization in PC /1 000 residents.

| Purpose of trip | 2020 | 2030 |
| --- | --- | --- |
|  | Min | Max | Average | Min | Max | Average |
| Individual | 74.6% | 81.0% | 77.0% | 76.4% | 82.3% | 78.6% |
| Public | 19.0% | 25.4% | 23.0% | 17.7% | 23.6% | 21.4% |

Table 24	Share of passenger services by mode of transport

Finally, trips by public transport were distributed among the coach and railway transport on the grounds of the generalized inferences. Summarized data on the national level are presented in the following table and diagram.

|  | Interzone passenger services |
| --- | --- |
|  | 2011 | 2020 | 2030 |
|  | total | share | total | share | total | share |
| Passenger cars | 444 186 | 71.8% | 465 982 | 73.1% | 511 111 | 74.3% |
| Coaches | 101 088 | 16.3% | 100 295 | 15.7% | 96 771 | 14.1% |
| Railway | 73 729 | 11.9% | 71 333 | 11.2% | 80 418 | 11.7% |
| Total | 619 003 | 100.0% | 637 611 | 100.0% | 688 300 | 100.0% |

Table 25	Summarized forecast on the growth in passenger services

- Railway		- Coach	- Passenger cars

Fig. 26	Summarized forecast on the growth in passenger services by modes of transport

# Forecast on the demand for freight transport

## 7.1	Forecast on the domestic freight services

The Consultant updated the forecast on growth in the demand for freight services by commodity groups in conformity with the methodology of BMFT: ‘By using the forecasts for growth in GVA from commercial goods, an assessment was made of the growth in tonnages by utilizing the trend for freight (the proportional contribution of each industrial sector to the total movement of freight) for each type of industry. Based on the standard connections for average tonnage carried over routes for various market sections, the following growth rates were obtained for the domestic freight transport’. The following table summarizes the forecasts from GTMP on the growth of freight automobile and freight railway transport and the elasticity of projected increases against the accumulated GDP growth by regions.

|  | GTMP 2008 |
| --- | --- |
|  | GDP growth | Growth automobiles | elasticity | Growth railway | elasticity | GDP growth | Growth automobiles | elasticity | Growth railway | elasticity |
|  | 2015/2008 | 2030/2008 |
| Northwestern | 4% | 6% | 1.50 | 13% | 3.25 | 45% | 68% | 1.51 | 101% | 2.24 |
| Northern central | 11% | 14% | 1.27 | 20% | 1.82 | 76% | 91% | 1.20 | 100% | 1.32 |
| Northeastern | 18% | 16% | 0.89 | 20% | 1.11 | 120% | 105% | 0.88 | 108% | 0.90 |
| Sofia | 36% | 25% | 0.69 | 10% | 0.28 | 207% | 147% | 0.71 | 74% | 0.36 |
| Blagoevgrad | 10% | 14% | 1.40 | 32% | 3.20 | 66% | 90% | 1.36 | 83% | 1.26 |
| Southwestern | 9% | 14% | 1.56 | 3% | 0.33 | 58% | 87% | 1.50 | 19% | 0.33 |
| Central Southern | 21% | 19% | 0.90 | 12% | 0.57 | 138% | 116% | 0.84 | 63% | 0.46 |
| Stara Zagora | 16% | 15% | 0.94 | 6% | 0.38 | 100% | 98% | 0.98 | 25% | 0.25 |
| Southeastern | 22% | 19% | 0.86 | 26% | 1.18 | 144% | 117% | 0.81 | 97% | 0.67 |

Table 26	Forecast on the growth in domestic freight services by automobile and railway transport from BMFT

In conformity with the methodology proposed in the Introductory Report the Consultant recalculated the estimated growth in freight services demand, as indicated in the following table with the updated forecast for growth in GDP and GVA by economic sectors.

|  | 2013 UPDATE |
| --- | --- |
|  | GDP growth | Growth automobiles | Growth railway | GDP growth | Growth automobiles | Growth railway |
|  | 2020/2011 | 2030/2011 |
| Northwestern | 4% | 6% | 13% | 17% | 25% | 38% |
| Northern central | 12% | 15% | 21% | 34% | 41% | 45% |
| Northeastern | 16% | 15% | 18% | 59% | 52% | 53% |
| Sofia | 42% | 29% | 12% | 129% | 91% | 46% |
| Blagoevgrad | 10% | 15% | 33% | 29% | 40% | 37% |
| Southwestern | 9% | 15% | 3% | 26% | 38% | 8% |
| Central Southern | 23% | 21% | 13% | 71% | 59% | 32% |
| Stara Zagora | 17% | 16% | 7% | 49% | 48% | 12% |
| Southeastern | 25% | 21% | 29% | 75% | 61% | 51% |

Table 27	Updated summarized forecast on the growth in domestic freight services by automobile and railway transport

As evident from the above tables, according to the updated forecast growth in the demand for freight transport services by 2030 will be more modest in comparison to the one projected in BMFT from GTMP.

## 7.2	Forecast on the international freight services

In conformity with the approach proposed in the Introductory report under the project the Contractor produced new forecasts on the growth in freight services on international destinations, relying on the forecasts from TRANS-TOOLS on increase in the commercial exchange between pairs of trading partners. TRANS-TOOLS is a model for forecasting the international transport flows, developed for the needs of the EC and recommended by the Commission as a reference one for the member countries. This model consists of 3 major parts:

- Global financial-commercial model (data on the import and export by countries) with a relevant methodology for forecasting

- Highly detailed database for the commercial exchange in natural and financial dimension by groups of commodities (about 3 000 kinds of commodities), which was updated for 2010 as a baseline year within the framework of the ETISplus project

- Forecasting tool for forecasting detailed volumes of trade, while taking into account the financial projection.

The most advantageous feature of this model is the complete taking into account of the global dimension of international trade instead of the usual limitations within the frames of a particular region. Furthermore, this approach ensures a high level of comparability with the EC reference model.

Presented in Schedule 5 is an extract from the estimation matrixes for growth in the automobile and railway transport by commodity groups.

A summary of forecasts on the demand for transport freight services is presented in the following table and diagram.

| thou. t. | 2011 | 2020 | 2030 |
| --- | --- | --- | --- |
|  | Automobile | Railway | Share RW | Automobile | Railway | Share RW | Automobile | Railway | Share RW |
| Domestic | 104 703 | 11 960 | 10.3% | 127 344 | 13 893 | 9.8% | 172 795 | 16 623 | 8.8% |
| International, incl. | 46 516 | 3 588 | 7.2% | 56 160 | 4 770 | 7.8% | 74 149 | 7 195 | 8.8% |
| Import | 21 172 | 954 | 4.3% | 25 953 | 1 316 | 4.8% | 34 743 | 1 925 | 5.3% |
| Export | 17 084 | 1 196 | 6.5% | 21 947 | 1 579 | 6.7% | 31 146 | 2 622 | 7.8% |
| Transit | 8 260 | 1 438 | 14.8% | 8 260 | 1 875 | 18.5% | 8 260 | 2 647 | 24.3% |

Table 28	Summarized updated forecast on the growth in freight overland services

Freight carried

thou. t/year              Automobile		Railway	           Automobile	            Railway	     Automobile	       Railway

- Domestic		- International

Fig. 27	Summarized updated forecast on the growth in freight overland services

# Modeling the infrastructure networks by 2020

The identification of bottlenecks requires to juxtapose the traffic on a given section of the infrastructure and its throughput. This makes it necessary for the Contractor to model the respective networks under ‘Do minimum’ scenario while reflecting in the model the characteristics of all projects that are in the process of execution and/or financing is provided and the start of their construction is imminent and is to be completed before the first projected horizon 2020. The list of such projects includes:

- Automobile roads:

- Finalization of the construction of ‘Trakia’ MW  – lot 4

- Construction of ‘Maritsa’ MW – lot 1 and lot 2

- Finalization of the construction of ‘Strouma’ MW - lots 1, 2 and 4

- ‘Hemus’ Motorway, section ‘SRR-Yana Road Junction’

- Finalization of the construction of section Shumen – Belokopitovo on the ‘Hemus’ MW

- Railway lines:

- Completion of the electrification and rehabilitation of the Plovdiv – Svilengrad railway line in its section Dimitrovgrad - Svilengrad

- Electrification and rehabilitation of the railway line Svilengrad – Turkish border

- Rehabilitation of the railway infrastructure in sections of the Plovdiv – Burgas railway line

- Modernization of the ‘Septemvri – Plovdiv railway section as part of the Trans-European Railway Network.

# Assignment of projected passenger and freight traffic to the models of infrastructure networks

The Consultant assigned the projected traffic to 2020 and 2030 to the models of infrastructure networks by 2020 under a ‘Do minimum’ scenario.

## 9.1	Passenger services

The following 4 maps present the projected traffic in number of passengers by sections of the respective networks.

Fig. 28	Projected yearly number of passengers by automobile transport (PC and coach) for 2020.

Fig. 29	Projected yearly number of passengers by automobile transport (PC and coach) for 2030.

Fig. 30	Projected yearly number of passengers by railway transport for 2020.

Fig. 31	Projected yearly number of passengers by railway transport for 2030.

## 9.2	Freight services

The following four maps present the projected traffic in tons by sections of the respective networks.

Fig. 32	Projected freight traffic in tons by automobile transport for 2020.

Fig. 33	Projected freight traffic in tons by automobile transport for 2030.

Fig. 34	Projected traffic in tons by railway transport for 2020.

Fig. 35	Projected freight traffic in tons by railway transport for 2030.

## 9.3	Identification of bottlenecks

Ultimately, the Consultant transformed the estimated matrixes  into number of passengers and tons, into number of transport vehicles. In view of the forecast on a growth in motorization the factors for average occupancy of passenger cars were adjusted, as follows:

- For daily trips – 1.6965 for 2020 and 1.5179 for 2030

- For business trips – 1.6797 for 2020 and 1.5029 for 2030

- For private trips – 2.1711 for 2020 and 1.9426 for 2030

The remaining factors for coach and automobile freight transport (by market segments) are preserved the same as in the baseline 2011.

The estimated summary matrixes thus obtained for 2020 and 2030 in number of MTV are assigned to the model of the road network under the ‘Do minimum’ scenario (Fig. 36 and 37). The assigned traffic is compared with throughput of the network by sections. For each separate section the ratio is calculated between the projected average 24-hour number of MTV and the throughput. The results for 2020 and 2030 are visualized in Fig. 38 and 39. Sections in which the ratio exceeds 0.6, i.e. the average 24-hour number of MTA is above 60% of the number that can freely pass through a cross-section of the respective section can be accepted as narrow ones. During peak traffic, of the kind observed during the usual 24-hour, weekly and seasonal variations of traffic intensity, there can occur jams in such sections.

Fig. 36	Average 24-hour yearly intensity of automobile traffic by 2020.

Fig. 37	Average 24-hour intensity of automobile traffic by 2030.

Fig. 38	Comparison between average 24-hour intensity of automobile traffic by 2020 and throughput of the road network by sections

Fig. 39	Comparison between average 24-hour yearly intensity of automobile traffic by 2030 and throughput of the road network by sections

# Schedules

Schedule 1	System of zoning, internal zones

| Zone № | Name | Municipality | Region |
| --- | --- | --- | --- |
| 44 | Bansko | Bansko | Blagoevgrad |
| 136 | Yakoruda | Belitsa | Blagoevgrad |
| 48 | Blagoevgrad | Blagoevgrad | Blagoevgrad |
| 142 | Gotse Delchev | Gotse Delchev | Blagoevgrad |
| 142 | Gotse Delchev | Garmen | Blagoevgrad |
| 143 | Kressna | Kressna | Blagoevgrad |
| 50 | Petrich | Petrich | Blagoevgrad |
| 40 | Razlog | Razlog | Blagoevgrad |
| 51 | Sandansky | Sandansky | Blagoevgrad |
| 141 | Satovcha | Satovcha | Blagoevgrad |
| 49 | Simitly | Simitly | Blagoevgrad |
| 143 | Kressna | Stroumyani | Blagoevgrad |
| 142 | Gotse Delchev | Hadjidimovo | Blagoevgrad |
| 136 | Yakorouda | Yakorouda | Blagoevgrad |
| 116 | Ruen | Aytos | Burgas |
| 117 | Burgas | Burgas | Burgas |
| 117 | Burgas | Kameno | Burgas |
| 17 | Karnobat | Karnobat | Burgas |
| 9 | Malko Tarnovo | Malko Tarnovo | Burgas |
| 11 | Nesebar | Nesebar | Burgas |
| 10 | Pomorie | Pomorie | Burgas |
| 66 | Primorsko | Primorsko | Burgas |
| 116 | Ruen | Ruen | Burgas |
| 65 | Sozopol | Sozopol | Burgas |
| 64 | Sredets | Sredets | Burgas |
| 3 | Sungurlare | Sungurlare | Burgas |
| 67 | Tsarevo | Tsarevo | Burgas |
| 111 | Beloslav | Avren | Varna |
| 12 | Aksakovo | Aksakovo | Varna |
| 111 | Beloslav | Beloslav | Varna |
| 112 | Byala | Byala | Varna |
| 20 | Varna | Varna | Varna |
| 110 | Devnya | Vetrino | Varna |
| 110 | Devnya | Valchedram | Varna |
| 110 | Devnya | Devnya | Varna |
| 112 | Byala | Dolni Chiflik | Varna |
| 113 | Provadia | Dalgopol | Varna |
| 113 | Provadia | Provadia | Varna |
| 110 | Devnya | Suvorovo | Varna |
| 68 | Veliko Tarnovo | Veliko Tarnovo | Veliko Tarnovo |
| 97 | Strazhitsa | Gorna Oryahovitsa | Veliko Tarnovo |
| 98 | Elena | Elena | Veliko Tarnovo |
| 98 | Elena | Zlataritsa | Veliko Tarnovo |
| 97 | Strazhitsa | Lyaskovets | Veliko Tarnovo |
| 96 | Pavlikeni | Pavlikeni | Veliko Tarnovo |
| 6 | Polski Trambesh | Polski Trambesh | Veliko Tarnovo |
| 74 | Svishtov | Svishtov | Veliko Tarnovo |
| 97 | Strazhitsa | Strazhitsa | Veliko Tarnovo |
| 96 | Pavlikeni | Suhindol | Veliko Tarnovo |
| 79 | Chuprene | Belogradchik | Vidin |
| 80 | Gramada | Boynitsa | Vidin |
| 77 | Bregovo | Bregovo | Vidin |
| 72 | Vidin | Vidin | Vidin |
| 80 | Gramada | Gramada | Vidin |
| 78 | Ruzhintsi | Dimovo | Vidin |
| 80 | Gramada | Kula | Vidin |
| 80 | Gramada | Makresh | Vidin |
| 77 | Bregovo | Novo Selo | Vidin |
| 78 | Ruzhintsi | Ruzhintsi | Vidin |
| 79 | Chuprene | Chuprene | Vidin |
| 87 | Kneja | Borovan | Vratsa |
| 87 | Kneja | Byala Slatina | Vratsa |
| 85 | Krivodol | Vratsa | Vratsa |
| 87 | Kneja | Kneja | Pleven |
| 86 | Hairedin | Kozloduy | Vratsa |
| 85 | Krivodol | Krivodol | Vratsa |
| 88 | Mezdra | Mezdra | Vratsa |
| 86 | Hairedin | Mizia | Vratsa |
| 73 | Oryahovo | Oryahovo | Vratsa |
| 88 | Mezdra | Roman | Vratsa |
| 86 | Hairedin | Hairedin | Vratsa |
| 27 | Gabrovo | Gabrovo | Gabrovo |
| 23 | Dryanovo | Dryanovo | Gabrovo |
| 57 | Sevlievo | Sevlievo | Gabrovo |
| 28 | Tryavna | Tryavna | Gabrovo |
| 21 | Balchik | Balchik | Dobrich |
| 15 | General Toshevo | General Toshevo | Dobrich |
| 106 | Dobrich | Dobrich | Dobrich |
| 106 | Dobrich | Dobrich rural | Dobrich |
| 13 | Каvarna | Каvarna | Dobrich |
| 105 | Tervel | Krushari | Dobrich |
| 105 | Tervel | Tervel | Dobrich |
| 14 | Shabla | Shabla | Dobrich |
| 126 | Djebel | Ardino | Kardjali |
| 126 | Djebel | Djebel | Kardjali |
| 127 | Kirkovo | Kirkovo | Kardjali |
| 25 | Krumovgrad | Krumovgrad | Kardjali |
| 125 | Kardjali | Kardjali | Kardjali |
| 127 | Kirkovo | Momchilgrad | Kardjali |
| 125 | Kardjali | Chernoochene | Kardjali |
| 43 | Bobov Dol | Bobov Dol | Kyustendil |
| 151 | Dupnitsa | Boboshevo | Kyustendil |
| 151 | Dupnitsa | Dupnitsa | Kyustendil |
| 150 | Rila | Kocherinovo | Kyustendil |
| 152 | Kyustendil | Kyustendil | Kyustendil |
| 152 | Kyustendil | Nevestino | Kyustendil |
| 150 | Rila | Rila | Kyustendil |
| 151 | Dupnitsa | Sapareva Banya | Kyustendil |
| 152 | Kyustendil | Treklyano | Kyustendil |
| 95 | Apriltsi | Apriltsi | Lovech |
| 93 | Lovech | Letnitsa | Lovech |
| 93 | Lovech | Lovech | Lovech |
| 94 | Yablanitsa | Lukovit | Lovech |
| 55 | Teteven | Teteven | Lovech |
| 95 | Apriltsi | Troyan | Lovech |
| 53 | Ugarchin | Ugarchin | Lovech |
| 94 | Yablanitsa | Yablanitsa | Lovech |
| 84 | Berkovitsa | Berkovitsa | Montana |
| 81 | Boychinovtsi | Boychinovtsi | Montana |
| 82 | Medkovets | Brussartsi | Montana |
| 81 | Boychinovtsi | Valchedram | Montana |
| 84 | Berkovitsa | Varshets | Montana |
| 83 | Chiprovtsi | Georgi Damyanovo | Montana |
| 45 | Lom | Lom | Montana |
| 82 | Medkovets | Medkovets | Montana |
| 56 | Montana | Montana | Montana |
| 83 | Chiprovtsi | Chiprovtsi | Montana |
| 81 | Boychinovtsi | Yakimovo | Montana |
| 144 | Peshtera | Batak | Pazardjik |
| 145 | Septemvri | Belovo | Pazardjik |
| 144 | Peshtera | Bratsigovo | Pazardjik |
| 58 | Velingrad | Velingrad | Pazardjik |
| 145 | Septemvri | Lesichevo | Pazardjik |
| 37 | Pazardjik | Pazardjik | Pazardjik |
| 135 | Panagyurishte | Panagyurishte | Pazardjik |
| 144 | Peshtera | Peshtera | Pazardjik |
| 144 | Peshtera | Rakitovo | Pazardjik |
| 145 | Septemvri | Septemvri | Pazardjik |
| 135 | Panagyurishte | Strelcha | Pazardjik |
| 70 | Breznik | Breznik | Pernik |
| 153 | Radomir | Zemen | Pernik |
| 153 | Radomir | Kovachevtsi | Pernik |
| 71 | Pernik | Pernik | Pernik |
| 153 | Radomir | Radomir | Pernik |
| 54 | Tran | Tran | Pernik |
| 91 | Belene | Belene | Pleven |
| 89 | Gulyantsi | Gulyantsi | Pleven |
| 89 | Gulyantsi | Dolna Mitropolia | Pleven |
| 90 | Cherven Bryag | Dolni Dabnik | Pleven |
| 90 | Cherven Bryag | Iskar | Pleven |
| 92 | Pordim | Levsky | Pleven |
| 91 | Belene | Nikopol | Pleven |
| 35 | Pleven | Pleven | Pleven |
| 92 | Pordim | Pordim | Pleven |
| 90 | Cherven Bryag | Cherven Bryag | Pleven |
| 146 | Assenovgrad | Assenovgrad | Plovdiv |
| 148 | Rakovsky | Brezovo | Plovdiv |
| 149 | Saedinenie | Kaloyanovo | Plovdiv |
| 39 | Karlovo | Karlovo | Plovdiv |
| 147 | Stamboliysky | Krichim | Plovdiv |
| 147 | Stamboliysky | Kuklen | Plovdiv |
| 146 | Assenovgrad | Laky | Plovdiv |
| 36 | Maritsa | Maritsa | Plovdiv |
| 147 | Stamboliyski | Perushtitsa | Plovdiv |
| 34 | Plovdiv | Plovdiv | Plovdiv |
| 61 | Parvomai | Parvomai | Plovdiv |
| 148 | Rakovski | Rakovski | Plovdiv |
| 147 | Stamboliyski | Rodopi | Plovdiv |
| 59 | Sadovo | Sadovo | Plovdiv |
| 39 | Karlovo | Sopot | Plovdiv |
| 147 | Stamboliyski | Stamboliyski | Plovdiv |
| 149 | Saedinenie | Saedinenie | Plovdiv |
| 149 | Saedinenie | Hisarya | Plovdiv |
| 131 | Kubrat | Zavet | Razgrad |
| 133 | Isperih | Isperih | Razgrad |
| 131 | Kubrat | Kubrat | Razgrad |
| 132 | Razgrad | Loznitsa | Razgrad |
| 132 | Razgrad | Razgrad | Razgrad |
| 133 | Isperih | Samuil | Razgrad |
| 132 | Razgrad | Tsar Kaloyan | Razgrad |
| 100 | Byala-Rousse | Borovo | Rousse |
| 100 | Byala-Rousse | Byala-Rousse | Rousse |
| 101 | Rousse | Vetovo | Rousse |
| 102 | Dve Mogili | Dve Mogili | Rousse |
| 102 | Dve Mogili | Ivanovo | Rousse |
| 101 | Rousse | Rousse | Rousse |
| 101 | Rousse | Slivo Pole | Rousse |
| 100 | Byala-Rousse | Tsenovo | Rousse |
| 104 | Alfatar | Alfatar | Silistra |
| 103 | Glavinitsa | Glavinitsa | Silistra |
| 24 | Dulovo | Dulovo | Silistra |
| 104 | Alfatar | Kainardja | Silistra |
| 75 | Silistra | Silistra | Silistra |
| 103 | Glavinitsa | Sitovo | Silistra |
| 76 | Tutrakan | Tutrakan | Silistra |
| 22 | Kotel | Kotel | Sliven |
| 7 | Nova Zagora | Nova Zagora | Sliven |
| 30 | Sliven | Sliven | Sliven |
| 2 | Tvarditsa | Tvarditsa | Sliven |
| 129 | Smolyan | Banite | Smolyan |
| 130 | Dospat | Borino | Smolyan |
| 52 | Devin | Devin | Smolyan |
| 130 | Dospat | Dospat | Smolyan |
| 128 | Nedelino | Zlatograd | Smolyan |
| 128 | Nedelino | Madan | Smolyan |
| 128 | Nedelino | Nedelino | Smolyan |
| 128 | Nedelino | Rudozem | Smolyan |
| 129 | Smolyan | Smolyan | Smolyan |
| 31 | Chepelare | Chepelare | Smolyan |
| 134 | Pirdop | Anton | Sofia |
| 42 | Bozhurishte | Bozhurishte | Sofia |
| 41 | Botevgrad | Botevgrad | Sofia |
| 46 | Godech | Godech | Sofia |
| 138 | Elin Pelin | Gorna Malina | Sofia |
| 137 | Kostenets | Dolna Banya | Sofia |
| 47 | Dragoman | Dragoman | Sofia |
| 138 | Elin Pelin | Elin Pelin | Sofia |
| 140 | Etropole | Etropole | Sofia |
| 139 | Zlatitsa | Zlatitsa | Sofia |
| 62 | Ihtiman | Ihtiman | Sofia |
| 134 | Pirdop | Koprivshtitsa | Sofia |
| 137 | Kostenets | Kostenets | Sofia |
| 38 | Kostinbrod | Kostinbrod | Sofia |
| 139 | Zlatitsa | Mirkovo | Sofia |
| 134 | Pirdop | Pirdop | Sofia |
| 140 | Etropole | Pravets | Sofia |
| 69 | Samokov | Samokov | Sofia |
| 33 | Svoge | Svoge | Sofia |
| 32 | Slivnitsa | Slivnitsa | Sofia |
| 139 | Zlatitsa | Chavdar | Sofia |
| 139 | Zlatitsa | Chelopech | Sofia |
| 160 | Sofia | Sofia | Sofia-city |
| 154 | Pancharevo | Pancharevo | Sofia-city |
| 155 | Kremikovtsi | Kremikovtsi | Sofia-city |
| 156 | Novy Iskar | Novy Iskar | Sofia-city |
| 157 | Lyulin | Lyulin | Sofia-city |
| 158 | Bankya | Bankya | Sofia-city |
| 159 | Vitosha | Vitosha | Sofia-city |
| 119 | Chirpan | Bratya Daskalovi | Stara Zagora |
| 118 | Nikolaevo | Gurkovo | Stara Zagora |
| 120 | Radnevo | Galabovo | Stara Zagora |
| 19 | Kazanlak | Kazanlak | Stara Zagora |
| 118 | Nikolaevo | Maglizh | Stara Zagora |
| 118 | Nikolaevo | Nikolaevo | Stara Zagora |
| 120 | Radnevo | Opan | Stara Zagora |
| 60 | Pavel Banya | Pavel Banya | Stara Zagora |
| 120 | Radnevo | Radnevo | Stara Zagora |
| 4 | Stara Zagora | Stara Zagora | Stara Zagora |
| 119 | Chirpan | Chirpan | Stara Zagora |
| 16 | Antonovo | Antonovo | Targovishte |
| 5 | Omurtag | Omurtag | Targovishte |
| 99 | Popovo | Opaka | Targovishte |
| 99 | Popovo | Popovo | Targovishte |
| 18 | Targovishte | Targovishte | Targovishte |
| 26 | Dimitrovgrad | Dimitrovgrad | Haskovo |
| 29 | Ivailovgrad | Ivailovgrad | Haskovo |
| 121 | Lyubimets | Lyubimets | Haskovo |
| 124 | Stambolovo | Madjarovo | Haskovo |
| 122 | Haskovo | Mineralni Bani | Haskovo |
| 121 | Lyubimets | Svilengrad | Haskovo |
| 123 | Harmanli | Simeonovgrad | Haskovo |
| 124 | Stambolovo | Stambolovo | Haskovo |
| 8 | Topolovgrad | Topolovgrad | Haskovo |
| 123 | Harmanli | Harmanli | Haskovo |
| 122 | Haskovo | Haskovo | Haskovo |
| 109 | Smyadovo | Veliki Preslav | Shumen |
| 107 | Kaolinovo | Venets | Shumen |
| 109 | Smyadovo | Varbitsa | Shumen |
| 108 | Novi Pazar | Gara Hitrino | Shumen |
| 107 | Kaolinovo | Kaolinovo | Shumen |
| 108 | Novi Pazar | Kaspichan | Shumen |
| 107 | Kaolinovo | Nikola Kozlevo | Shumen |
| 108 | Novi Pazar | Novi Pazar | Shumen |
| 109 | Smyadovo | Smyadovo | Shumen |
| 1 | Shumen | Shumen | Shumen |
| 114 | Elhovo | Bolyarovo | Yambol |
| 114 | Elhovo | Elhovo | Yambol |
| 63 | Straldja | Straldja | Yambol |
| 115 | Yambol | Toundja | Yambol |
| 115 | Yambol | Yambol | Yambol |

Schedule 2	System of zoning, international zones

| Country name | Zone name | Zone code |
| --- | --- | --- |
| ALBANIA | ALBANIA | AL |
| AUSTRIA | AUSTRIA | AT |
| BOSNIA AND HERZEGOVINA | BOSNIA AND HERZEGOVINA | BA |
| BELGIUM | Benelux | BNL |
| LUXEMBOURG | Benelux | BNL |
| HOLLAND | Benelux | BNL |
| CZECH REPUBLIC | CZECH REPUBLIC | CZ |
| GERMANY | Southern Germany | DE1 |
| GERMANY | Sorthern Germany | DE2 |
| DENMARK | Scandinavia | DK |
| NORWAY | Scandinavia | DK |
| FINLAND | Scandinavia | DK |
| SWEDEN | Scandinavia | DK |
| ESTONIA | Baltic states | ЕЕ |
| LATVIA | Baltic states | EE |
| LITHUANIA | Baltic states | EE |
| ANDORRA | Spain and Portugal | ES |
| GIBRALTAR | Spain and Portugal | ES |
| SPAIN | Spain and Portugal | ES |
| PORTUGAL | Spain and Portugal | ES |
| FRANCE | Northern France | FR1 |
| LIECHTENSTEIN | Southern France | FR2 |
| MONACO | Southern France | FR2 |
| FRANCE | Southern France | FR2 |
| GREECE | Greece – Eastern Macedonia and Thrace | GR1 |
| GREECE | Greece – Central Macedonia | GR2 |
| GREECE | Greece – the remaining part | GR3 |
| SLOVENIA | SLOVENIA | HR |
| CROATIA | CROATIA | HR |
| HUNGARY | HUNGARY | HU |
| ITALY | Southern Italy | IT1 |
| ITALY | Northern Italy | IT2 |
| SAN MARINO | Northern Italy | IT2 |
| SWITZERLAND | Northern Italy | IT2 |
| MACEDONIA | Northern Macedonia / Skopie | MK1 |
| MACEDONIA | Southern Macedonia | MK2 |
| POLAND | POLAND | PL |
| ROMANIA | Northeastern Romania | RO5 |
| ROMANIA | Eastern Romania | RO1 |
| ROMANIA | Southern Central Romania | RO2 |
| ROMANIA | Southwestern Romania | RO3 |
| ROMANIA | Northwestern Romania | RO4 |
| SERBIA | Vojvodina | RS1 |
| SERBIA | Central Serbia | RS2 |
| SERBIA | Southern Serbia | RS3 |
| BELARUS | Russia and Belarus | RU |
| RUSSIA | Russia and Belarus | RU |
| SLOVAKIA | SLOVAKIA | SK |
| TURKEY | TURKEY | TR |
| GREAT BRITAIN | Great Britain and Ireland | UK |
| IRELAND | Great Britain and Ireland | UK |
| MOLDOVA | the Ukraine and Moldova | UR |
| THE UKRAINE | the Ukraine and Moldova | UR |
| KOSOVO | KOSOVO | XK |
| Other | Rest of the world | XXXX |

Schedule 3	Foreigners visiting Bulgaria, by purpose of travel and by country, for 2011

| Countries | Total | Purpose of travel |
| --- | --- | --- |
|  |  | Holidays and excursion | Business | Other |
| T O T A L | 8 702 585 | 4 475 735 | 970 542 | 3 256 308 |
| European Union | 5 540 949 | 4 475 735 | 970 542 | 3 256 308 |
| Incl. |  |  |  |  |
| Austria | 186 438 | 74 081 | 43 590 | 68 767 |
| Belgium | 91 947 | 47 957 | 16 135 | 27 855 |
| Great Britain | 306 939 | 221 866 | 41 928 | 43 145 |
| Germany | 836 845 | 571 696 | 91 592 | 173 557 |
| Greece | 1 120 640 | 554 051 | 218 486 | 348 103 |
| Denmark | 81 860 | 63 538 | 8 887 | 9 435 |
| Ireland | 29 941 | 19 319 | 3 762 | 6 860 |
| Spain | 60 026 | 32 550 | 13 718 | 13 758 |
| Italy | 130 259 | 50 760 | 39 664 | 39 835 |
| Cyprus | 21 157 | 9 204 | 5 320 | 6 633 |
| Malta | 4 178 | 2 464 | 873 | 841 |
| the Netherlands | 149 449 | 77 054 | 13 688 | 58 707 |
| Poland | 289 742 | 208 076 | 22 260 | 59 406 |
| Portugal | 9 099 | 5 977 | 2 537 | 585 |
| Romania | 1 499 415 | 597 546 | 182 559 | 719 310 |
| Slovakia | 94 355 | 47 215 | 8 734 | 38 406 |
| Slovenia | 22 140 | 12 163 | 6 223 | 3 754 |
| Hungary | 123 735 | 73 079 | 21 656 | 29 000 |
| Finland | 43 570 | 33 049 | 2 663 | 7 858 |
| France | 182 407 | 106 454 | 29 366 | 46 587 |
| Czechia | 176 135 | 129 500 | 17 112 | 29 523 |
| Sweden | 49 492 | 35 399 | 6 321 | 7 772 |
| Other EU | 31 180 | 20 130 | 4 931 | 6 119 |
| Norway | 48 707 | 44 592 | 1 469 | 2 646 |
| Republic of Macedonia | 439 679 | 316 100 | 11 381 | 112 198 |
| Russia | 469 772 | 350 969 | 50 039 | 68 764 |
| Serbia | 365 644 | 213 898 | 5 592 | 146 154 |
| Turkey | 860 654 | 21 570 | 46 765 | 792 319 |
| the Ukraine | 251 803 | 129 083 | 11 721 | 110 999 |
| Switzerland | 38 476 | 22 616 | 3 092 | 12 768 |
| Israel | 138 951 | 134 016 | 3 148 | 1 787 |
| Canada | 14 849 | 12 045 | 731 | 2 073 |
| USA | 65 483 | 51 492 | 6 130 | 7 861 |
| Rest of the world | 467 618 | 186 226 | 28 469 | 252 923 |

Schedule 4	Trips abroad by Bulgarian nationals in 2011, by country

| Countries | Total | Purpose of travel |
| --- | --- | --- |
|  |  | Holidays and excursion | Business | Other |
| T O T A L | 3 803 240 |  |  |  |
| European Union | 1 935 405 |  |  |  |
| incl. |  |  |  |  |
| Austria | 54 461 | 20 949 | 27 703 | 5 809 |
| Belgium | 28 022 | 9 180 | 14 864 | 3 978 |
| Great Britain | 77 675 | 18 046 | 38 954 | 20 675 |
| Germany | 163 314 | 52 297 | 94 860 | 16 157 |
| Greece | 1 000 660 | 334 338 | 549 884 | 116 438 |
| Denmark | 2 803 | 620 | 1 616 | 567 |
| Ireland | 1 186 | 252 | 149 | 785 |
| Spain | 77 496 | 29 151 | 41 171 | 7 174 |
| Italy | 70 272 | 26 133 | 39 691 | 4 448 |
| Cyprus | 12 896 | 3 656 | 7 656 | 1 584 |
| Malta | 1 118 | 483 | 529 | 106 |
| the Netherlands | 23 082 | 8 223 | 12 279 | 2 580 |
| Poland | 17 584 | 6 975 | 8 790 | 1 819 |
| Portugal | 2 004 | 1 140 | 778 | 86 |
| Romania | 327 555 | 125 138 | 175 369 | 27 048 |
| Slovakia | 1 260 | 333 | 847 | 80 |
| Slovenia | 2 313 | 837 | 1 306 | 170 |
| Hungary | 17 304 | 4 231 | 9 569 | 3 504 |
| Finland | 380 | 85 | 182 | 113 |
| France | 31 010 | 9 359 | 19 355 | 2 296 |
| Czechia | 20 022 | 7 004 | 11 275 | 1 743 |
| Sweden | 1 851 | 539 | 974 | 338 |
| Other EU | 1 137 | 205 | 839 | 93 |
| Norway | 1 742 | 277 | 457 | 1 008 |
| Republic of Macedonia | 305 536 | 51 519 | 98 230 | 155 787 |
| Russia | 14 157 | 3 997 | 7 337 | 2 823 |
| Serbia | 295 135 | 149 182 | 127 604 | 18 349 |
| Turkey | 1 178 547 | 175 153 | 213 257 | 790 137 |
| the Ukraine | 8 892 | 1 962 | 5 722 | 1 208 |
| Switzerland | 9 389 | 3 133 | 5 155 | 1 101 |
| Israel | 5 655 | 609 | 3 914 | 1 132 |
| Canada | 1 477 | 62 | 151 | 1 264 |
| USA | 5 931 | 325 | 862 | 4 744 |
| Rest of the world | 41 374 | 15 219 | 19 317 | 6 838 |

Schedule 5	Extract from a TRANS-TOOLS matrix for growth in the road transport freightage

| From | To | Commodity group | 2011-2020 | 2011-2030 |
| --- | --- | --- | --- | --- |
| BG | DE | 0 | 1.184066 | 1.42858 |
| BG | DE | 9 | 1.494821 | 2.336562 |
| BG | FR | 0 | 1.275205 | 1.670671 |
| BG | FR | 9 | 1.376946 | 1.964576 |
| BG | HU | 1 | 1.51215 | 2.394113 |
| BG | IT | 4 | 1.016865 | 1.035938 |
| BG | RO | 6 | 1.860066 | 3.706843 |
| BG | RS | 8 | 1.194249 | 1.454642 |
| AT | BG | 5 | 1.342531 | 1.862355 |
| AT | BG | 8 | 1.349446 | 1.882664 |
| GR | BG | 1 | 1.589775 | 2.660982 |
| HU | BG | 8 | 1.207274 | 1.488337 |
| IT | BG | 9 | 1.219136 | 1.519379 |
| PL | BG | 9 | 1.608902 | 2.729021 |
| TR | BG | 0 | 1.434436 | 2.141762 |
| TR | BG | 5 | 1.361831 | 1.919327 |
| CZ | TR | 0 | 1.403117 | 2.044239 |
| DE | GR | 9 | 1.018694 | 1.039874 |
| DE | TR | 1 | 1.298403 | 1.735481 |
| RO | GR | 5 | 1.182498 | 1.42459 |

Schedule 6	Extract from a TRANS-TOOLS matrix for growth in the railway transport freightage

| From | To | Commodity group | 2011-2020 | 2011-2030 |
| --- | --- | --- | --- | --- |
| BG | GR | 0 | 1.305229 | 1.7548 |
| BG | GR | 8 | 1.099645 | 1.222048 |
| BG | HU | 3 | 1.381977 | 1.979762 |
| BG | HU | 9 | 1.228182 | 1.543276 |
| BG | RO | 2 | 0.84802 | 0.706086 |
| GR | BG | 8 | 1.45064 | 2.19316 |
| GR | HU | 4 | 0.712124 | 0.488347 |
| GR | HU | 6 | 1.622274 | 2.777125 |
| GR | RO | 4 | 1.251058 | 1.604587 |
| HU | BG | 6 | 1.075403 | 1.165871 |
| BG | TR | 8 | 1.490068 | 2.320903 |
| GR | BG | 5 | 1.689622 | 3.026142 |
| HU | TR | 1 | 1.536367 | 2.475778 |
| HU | TR | 6 | 0.704902 | 0.47795 |
| RO | BG | 2 | 1.183752 | 1.427781 |
| RO | GR | 5 | 1.182498 | 1.42459 |
| TR | BG | 5 | 1.361831 | 1.919327 |
| TR | RO | 4 | 1.456413 | 2.211625 |
| BG | GR | 9 | 1.164239 | 1.37855 |
| BG | RO | 4 | 1.323128 | 1.80599 |

# Footnotes

GTMP Main Report 1, p. 8

GTMP Main Report 1, p. 7

GTMP Main Report 1, p. 8

GTMP Main Report 3, p. 10

GTMP Main Report 3, p. 25

GTMP Main Report 3, p. 28

GTMP Main Report 3, p. 47, Table 3.29

GTMP volume 1, it. 5.2.5 Synthetic demand, p. 29

GTMP, volume 1, it. 7.2.3 Time values, p.

NSI, 2011 Census of the population and housing, volume 1 Population, book 7 Daily trips

Source: CAA DG, http://caa.gateway.bg/page.php?category=27

Source: GTMP

Source: Central Institute of Toad Technology, National and European Norms and Standards

http://www.rta.government.bg/rts.html

Coach lines on the regional and municipal transport schemes are not included in the survey, as it was assumed that they are used basically for interzone trips

GTMP, volume 1, it. 5.3.6 Summarization

Following the introduction of the vignette system in 2004 the RIA does not collect toll from foreign MTV, and border control of passengers was discontinued at internal borders since 2007.

Source: BDZ Passenger Transport EOOD

Source: MTITC as Contracting Authority

Excluded Smolyan Region, where no railway transport is available

Source: Passenger trains by sections and lines, ‘NRIC’ SE

Source: Railway Administration EA

Source: NSI http://www.nsi.bg/otrasal-metodologia.php?otr=6

Data about freight via sea and river ports are in compliance with Ordinance № 919 of 2000 on the collection of statistical information about the activity of port operators and owners of ports and port facilities in R of Bulgaria.

http://www.nsi.bg/otrasal-metodologia.php?otr=60

GTMP, volume 3, Analysis of the future transport demand, it. 2.2.4 Overall Growth, p. 7

Source: data MF

Source: JASPERS Bulgaria

GTMP, volume 3 Analysis of the future transport demand, it. 2.3.2 GDP growth by regions, p. 11

Regions, as defined in BMPT and BMFT

Source: http://www.nsi.bg/otrasal.php?otr=19&a1=376&a2=387&a3=389#cont

GTMP, volume 3 Analysis of the future transport demand, it. 2.2.5 Projected demand by mode of transport

412 PA/1 000 residents by 2030, GTMP, volume 3 Analysis of the future transport demand, it. 2.6 Ownership in means of transport, Table 2.16, p. 21

GTMP, volume 3 Analysis of the future transport demand, it. 2.2.5 Estimated demand by forms of transport, Table 2.1, p. 9

GTMP, volume 3 Analysis of the future transport demand, it. 2.5.5 Prices of public transport, p. 19

GTMP, volume 3 Analysis of the future transport demand, it. 2.2.5 Projected demand by mode of transport, p. 8

GTMP, volume 3 Analysis of the future transport demand, it. 3.3.3.5 General domestic forecasts, p. 36

GTMP, volume 3 Analysis of the future transport demand, Table 3.12 and 5.4

TRANS-TOOLS: TOOLS for TRansport forecasting ANd Scenario testing; http://energy.jrc.ec.europa.eu/transtools/

ETISplus – European Transport policy Information System http://www.etisplus.eu/default.aspx